## Slide 1
Application of modern commercial digitizers for new approaches to neutron's detection
Dmitrii Ponomarev
2019

## Slide 2
Modern digitizers

## Slide 3
Low background experiments

## Slide 4
Neutron’s detectors
n+ 3He  3H+ 1H+764keV
Thermal neutron cross section
of 3He = 5333±7 barns
6Li+n → t + α +4.79 MeV
Thermal neutron cross section
of 6Li = 940barns
Pulse shape discrimination neutron’s from gamma’s
3He- neutron detectors
6Li- neutron detectors

## Slide 5
CLYC (Cs2LiYCl6: Ce) detector
Crystal dimensions: 38X38mm
Energy resolution 662keV: ≈ 5.8%
6Li enrichment: ≈ 96%
CLLB (Cs2LiLaBr6: Ce) detector
Crystal dimensions: 51X51mm
Energy resolution 662keV: ≈ 4.3%
Natural lithium- 6Li ≈ 7,5%

## Slide 6
NaIL (NaI(Tl+Li)) detector
Crystal dimensions: 127X152mm
Energy resolution 662keV: ≈ 6.7%
6Li concentration: ≈ 1% of mass of the detector
CAEN DT5790
Sampling Rate: 250 MS/s simultaneously on each channel
Resolution: 12 bits

## Slide 7
PSD diagram and neutron flux for CLYC detector
neutrons
1x10-3 n cm-2 sec-1
α- particles

## Slide 8
Contaminations in the 6Li containing detectors
CLLB background spectra
CLYC and NAIL detectors:
Contamination by 238U chain
Daughter isotopes has alpha-activity in zone of interest
CLLB detector:
Contamination by 227Ac chain
Daughter isotopes has alpha-activity in zone of interest.
Significant 138La contamination in gamma spectrum.

## Slide 9
NaI (solid) has 545 times as many moles as an
equal volume of 3He (gas, normal pressure)
Iodine has only one stable isotope: 127I
σγ = 6.2(2) barn (860 times lower than 3He)
Efficiency of thermal neutron capture in 1 kg NaI detector is ~50% (almost all captures will be on iodine because for 23Na: σγ = 0.9(1) barn)
Result of neutron capture is 128I in 6.8 MeV excited state
Neutron measurements with NaI
128I decay to the ground state proceeds through a series of low-energy levels
128I has 137.8 keV isomeric state T1/2 = 0.845(20) µsec
~40% de-excitations pass through the 137.8 keV level
Delayed coincidences to identify neutrons

## Slide 10
Test in with NaI Dubna
NaI(Tl) Ø63 mm x 63 mm
PMT Hamamatsu R6091
CAEN Multi channel analyzer DT5780
Tprompt – T delay = 1.8-5 µsec
Simultaneous measurement with bare 3He detector

## Slide 11
Cut:
Tprompt – T delay = 1.8-5 µsec, Prompt: ADC channels >300
Results:
For ADC channel (delayed) 380-460, i.e. neutrons
1.8 - 5 µsec: 70 events
Expected background (calculation) 33,969 ± 0,003 events
Measured 11.8 -15 µsec: 37 events
Flux = 2.1 ± 0.5 × 10-6 cm-2 sec-1
same as 3He detector on the top (2.3 × 10-6 cm-2 sec-1),
about 30% less than 3He detector
located near the wall (3.1 × 10-6 cm-2 sec-1)
137.8 keV
Result after 260.45 days
ADC channels
Counts/260.45d

## Slide 12
neutrons
α- particles
PSD diagram and neutron flux for NAIL detector
I-127
Li-6

## Slide 13
Ambient neutron background with CLYC, CLLB and NAIL detectors were measured
Results of the measurement showed good sensitivity of mentioned detectors to small changes in neutron flux on the level 10-3 n cm-2 s-1
These detectors can be well used in strong or even on ground level neutron fields
Unfortunately, high intrinsic background make CLYC, CLLB and ,for now, NAIL detectors inapplicable for low background environments.
Modern commercial digitizers makes it possible to find new ways for neutron detection as with completely new detectors, as and with well known old ones.
Conclusion