MPD
Software
development
status
MPD Coll. meeting
 April 16, 2019
Dubna
ROGACHEVSKY Oleg
for MPD collaboration

---
Nuclotron based Ion Collider fAcility

---
MPD experiment

---
Detectors simulation status
 GitLab repository: https://git.jinr.ru/nica/mpdroot
Detector	MC Geometry	Hits/digits
TPC	Ver. 8 (2018)	hitproducer
TOF	Ver. 7 (2016)	hitproducer
ECAL	Ver. 8 (2018)	hitproducer
FHCal	Ver. 2 (2018)	hitproducer
ITS	Ver. 3 (2015)	hitproducer
FFD	Ver. 0 (2016)	hitproducer
BBC	Ver. 2 (2019)	MC points

---
MPD.jinr.ru
The framework MpdRoot is based on ROOT and FairRoot and developed for the MPD event simulation, reconstruction of experimental or simulated data and following physical analysis of heavy ion collisions registered by the MultiPurpose Detector at the NICA collider.

---
MPDRoot design

---
TPC geometry ver.8
Root geometry
Drawing
35 000 nodes

---
Electronics Simulation
Each board:
----------------------------------------------------------
2+1 mm Copper
----------------------------------------------------------
3,5 mm Textolite
Flat cable:
----------------------------------------------------------
0,1+0,1 mm
Polypropylene
Insulation
----------------------------------------------------------
0,15 mm
Copper wire
Connector to
Pads plane:
----------------------------------------------------------
Plastic + Air gap

---
TPC material budget
Looking in TPC detector with geantino
Material budget
 for TPC
Material budget
 for all MPD detectors
40○

---
TPC gas and ROC properties
Garfield++
Version 2019.3

---
Beam Beam monitoring
ArXiv:1809.10553
The MPD beam-beam monitoring system is considered as a part of level-0 trigger. Its time resolution is expected to be around 30 ps. To fulfill the trigger requirements the BE-BE geometry consists of two hodoscope detectors, each located 2 meters away from the interaction point, at opposite sides. Each detector consists of an array of 162 hexagonal plastic scintillator cells arranged in six concentric rings. It covers a pseudorapidity range of 1.9 < |η| < 3.97.
 The BE-BE’s trigger signal will be useful to generate a trigger logic to identify and discriminate beam-beam events, either for minimum bias or with a given centrality, from background and beam-gas interactions.
 Estimated event plane resolution using the BE-BE

---
Current & Future Tasks
rogachevsky@jinr.ru
Manpower
Boost clustering in detectors,
Boost tracking,
Detectors alignment and calibrations,
Cloud computing for the MPD experiment,
Virtual organisation for MPD in GRID,
….
Physics analyses ...

---
Clustering in MPD TPC
The hit reconstruction algorithm contains the following main steps:
Searching for extended clusters in (Pad-Time) for each pad raw.
Searching for peaks in time-profile for each pad in the found extended cluster.
Combining the neighboring peaks into resulting hits.

---
Event Display for the NICA experiments
 EventDisplay for the MPD experiment
MPD event data:TPC hits
 and EMC towers
Au-Au Elab = 4.GeV
Au-Au √sNN = 7.GeV

---
Data in the LHEP cluster
nc*.jinr.ru

---
Migrate to HybriLIT (hlit.jinr.ru)

---
Event generators & reco data databases in HybriLIT farm
Generator	# of events / 106
QGSM	4
UrQMD	~ 4
PHSD	4
vHLLE_UrQMD	~ 4
3FD(Theseus)	5
Hybrid UrQMD	3

---
Computing for MPD in HybriLIT
Data storage organization
“Cold” Data Storage
“Hot” Data Storage
Lustre FS
Data flow organization
Particles Generator
- internal
- external
MpdRoot
Simulation & reconstruction framework
Experiment
Data Management System
EOS FS
ZFS FS

---
Thank for your attention