## Slide 1: Vertex detector: status report
N. Zamyatin on behalf SPD JINR- group
International Workshop “SPD at NICA-2019”
7 June 2019

## Slide 2: Performance requirements of the Inner Tracker
From general conditions:
Close to 4π geometry;
Number of coordinate layers: 5 + 3;
Inner Tracker (Version-1, CDR) based on two types Si-sensors:
Double Side Silicon Detector (DSSD) – outer 5 layers;
MAPS (Monolitic Active Pixel Sensor) – inner 3 layers
Material budget of 1 layer DSSD include:
- Si (300 μm)= 0,003;
- Polyimide cable = 0,0016(1 cable) 0,0048 (3 cables);
- Carbon frame=0,005;
Barrel cover up to |η| =1,15;
End-cap cover up to |η| =2,5;
Track reconstruction efficiency for muons >99% at p 13 GeV/c (for 0≤|η|≤2,5);
Coordinates resolutions: < 50 μm, < 100 μm.

## Slide 3
Region of VD
|η| =1.5
|η| =1
|η| =2.5
|η| =0.5
Range system
Electromagnetic calorimeter
PID
Barrel Si-MAPS
Barrel Si-DSSD
Tracking system
|η| =1.15
|η| =2
SPD facility

## Slide 4
|η| =1.5
|η| =1
|η| =2.5
|η| =2
|η| =0.5
|η| =1.15
Barrel Si-MAPS
Barrel Si-DSSD
End Cap Si-MAPS
End Cap Si-DSSD
Fig.2 Cross-section of Inner Tracker
Primary goal of IT: determine coordinates of primary and secondary vertexes for rejection of physical background ( for DY processes)

## Slide 5
Vertex Detector Layout
General view of Vertex Detector (left) and -plane (right)
Barrel Si-MAPS
Barrel Si-DSSD

## Slide 6
Front-End Electronics
Carbon fiber ladder
Si -modules
View of carbon fiber ladder with Si-modules
Laying modules on carbon fiber support.
Puts from center to edge.
Electronics located at the edges of the ladder.
Polyimide cables
Front-End Electronics
[see B. Topko talk]

## Slide 7
 | Number of Sensors per ladder | Number of ladders | Number of Sensors | Area, m2 Area of 1 MAPS 4,5 cm2 Area of 1 DSSD 40 cm2
1 layer – MAPS | 10 | 12 (L=150 мм) | 10×12 = 120 | 0,054
2 layer – MAPS | 18 | 20 (L=270 мм) | 18×20 = 360 | 0,162
3 layer – MAPS | 26 | 28 (L=390 мм) | 26×28 = 728 | 0,327
4 layer – DSSD | 8 | 19 (L= 496 мм) | 8×19 = 152 | 0,603
5 layer – DSSD | 10 | 23 (L=620 мм) | 10×23 = 230 | 0,912
6 layer – DSSD | 12 | 27 (L=746 мм) | 12×27 = 324 | 1,285
7 layer – DSSD | 14 | 31 (L=870 мм) | 14×31 = 434 | 1,722
8 layer – DSSD | 16 | 35 (L=996 мм) | 16×35 = 560 | 2,222
Total for barrel |  |  | Number of MAPS = 1208 | Total area MAPS =0,54 m2
 |  |  | Number of DSSD = 1700 | Total area DSSD = 6,74 m2
Total barrel + 2 end-cap: |  | Cost estimation (1,5 Meuro/m2)
Number of MAPS = 1798 | Total area MAPS = 0,804 m2 | 1,5 Meuro
Number of DSSD = 2096 | Total area DSSD =8,32 m2 | 12,5 Meuro

## Slide 8: Attention
Tracker system based on silicon detectors is the most expensive part of SPD facility. It’s important to remember that:
Cost of barrel layers is proportionally R2 и Lz
Main goal – optimization Vertex Detector construction (decrease the active area and keep satisfaction for physics requirements)

## Slide 9: Possible versions of Vertex Detector design
Version - 1 (CDR):
Double Side Silicon Detector (DSSD - outer 5 layers) and Monolitic Active Pixel Sensor (MAPS - inner 3 layers)
Version – 2 (full MAPS):
Monolitic Active Pixel Sensor (MAPS) - 3 or 5 layers
Version – 3 (full DSSD):
- Double Side Silicon Detector (DSSD) - 8 or 5 layers

## Slide 10
Parameter | MAPS - sensors | DSSD - sensors
Resolution-pitch, mkm | 5/30 | 30/95
Material budget/layer, % Х0 | 0.3 | 0.3 (Si-300mkm) + 0.16÷0.48 (polyimid cables)
FE-chip | FE-electronics integrated on MAPS | Need to choice of the type FE-ASIC chip-128 ch (need collaboration with ASICs development centers)
Power, mW/cm2 | 100 mW/cm2 | 250 mW/chip (10 chips per 80 cm2 of Si-DSSD is equal 2.5 W)
Cooling | Cooling of the full area ladders | Cooling only FE-chips area
cable | Cables from ladders to DAQ | Cables-1 from sensors to FE and cables-2 from FE to DAQ
Staging | yes | yes
Commercial available | ? | yes
Assembling process | in collaboration with CERN, experience of ALICE-upgrade and VD-MPD | Based on BM@N assembly process + experience of JINR team (Yu. Murin) in CBM
Radiation hardness | Not full depleted pixel (1013 neq/cm2) | Up to 5×1014 neq/cm2 (with cooling of Si)
∆E from VD layers | impossible | +

## Slide 11: FE-ACICs
 | APV25 | VATAGP7.3 | n-XYTER | TIGER | ???
Channels number | 128 | 128 | 128 | 64 (128?) | 
Dynamic Range | -40fC ÷ 40fC | -30fC ÷ 30fC | Input current 10nA Polarity - and+ | 1÷50fC | 
Gain | 25mV/fC | 20µA/fC |  | 10.35mV/fc | 
Noise | 246e-+36 e-/pF | 70e-+12 e-/pF | 900e- at 30pF | 2000e- at 100pF | 
Peaking time | 50ns | 50ns/500ns | 30ns/ 280ns | 60ns/ 170ns | 
Power consumption | 1.15mW/ch. | 2.18mW/ch. | 10mW/ch. | 12mW/ch. | 
ADC | No | No | 16fC, 5 bit | 10-bit Wilkinson ADC | 
TDC | No | No |  | 10-bit Wilkinson ADC | 
Output | Multiplexing single end diff. signal. | Multiplexing single end diff. signal.20MHz | 4x500Mbit/s LVDS | 4x640Mbit/s LVDS | 

## Slide 12: Summary
Conceptual design of Vertex Detector SPD in progress (few version: based on full DSSD layers, full MAPS layers and combined (DSSD + MAPS) detector construction);
These versions will be use for SPD simulation;
At this moment R&D focused on reduce active area, material budget and power dissipation of the tracker;
Finally version should be accept after full Monte-Carlo simulation.

## Slide 13: Backup slides

## Slide 14: New ITS design

## Slide 15
ALPIDE Chip

## Slide 16: CMOS Pixel Sensor
Schematic of MAPS pixel
in imaging CMOS TowerJazz 0.18 μm technology
TowerJazz 0.18μm CMOS Imaging Process
Pixel pitch ~ 30 μm
High-resistivity (> 1kΩ cm) p-type
epitaxial layer (25μm) on p-type substrate
Small n-well diode (2 μm diameter),
=> low capacitance
Reverse bias voltage to substrate
(contact from the top) can be used
to increase depletion zone around NWELL collection diode
Deep PWELL shields NWELL of PMOS
Transistors
Very low power dissipation
J. Phys. G: Nucl. Part. Phys. 41 (2014) 087002

## Slide 17
Size: 63x63x0,3 mm3 (on 4” – FZ-Si wafers)
Topology: double side microstrip (DSSD) (DC or AC coupling)
Pitch p+ strips: 95 μm;
Pitch n+ strips 190 μm;
Stereo angle between p+/n+ strips: 900
Number of strips: 640 (p+)320(n+)
Detector’s topology

## Slide 18
DSSD with DC topology don’t contain integral resistors and capacitors (RC), therefore external R, C are required to supply bias voltage to each strip and to electrically decouple the DC current from the electronic inputs. This role is performed by Pitch Adapter (PA) with a topology of two types for p+ and n+ sides of the detector. In addition, PA has topology of contact pads similar to chips located on the side of electronic chips. PA modules are made on sapphire plates with an epitaxial layer of silicon (SOI). Integrated poly silicon bias resistors have a value of 0.7 – 1.0 MΩ, decoupled capacitors have a value of 140 pF. PA is assembled together with read-out ASICs on the read-out card. Positive polarity signals come from detectors to P+ read-out card (black PCB) while negative signals come to N+ read-out card (red PCB).
The functional scheme of detector module and appearance of two electronic boards
(FE-design of BM@N experiment)

## Slide 19: Parameters of new read-out chip
Readout ASIC VATAGP7.3.
Number of sensitive pre-amplifier (CSA) inputs – 128
Input charges (dynamic range) - -30fC ÷ +30fC
Peaking time (slow shaper) - 500ns (typ.)
Peaking time (fast shaper) - 50ns
Noise (ENC)- 70e +12e/pF (typ.)
Lowest threshold (no capacitance) 0.12fC
Good linearity for charges up to +/- 15fC
Gain from input to output buffer (diff. output currents) 16.5µA/fC
Output Serial analog multiplexer with 20 MHz clock speed nominal.
Voltage supply - +1.5V, -2.0V
Power dissipation per channel – tbd
We are waiting delivery of first 10 ASICs at the end of Q2 2019

## Slide 20: Polyimide cable
Signal cable
Perforated dielectric strip (perforation area 70%)
Shielding layer with gasket
The combination of signal and shielding layers
Additional holes for combining layers
Resistance of one conductor (1200■): | 0,96 Ω
Specific resistance: | 0,8
Electrical capacitance between conductors: | 16 ± 2 pF
Resistance of one conductor (1200■): | 0,96 Ω
Specific resistance: | 
Electrical capacitance between conductors: | 16 ± 2 pF
33 aluminum conductors (width 0.5 mm)
Cable positioning holes
3 rows of windows for unwelding conductors
Manufacturing: Light Technologies Ukraine. Ukraine, Kharkov
viatcheslav.borshchov@cern.ch, maksym.protsenko@cern.ch
Maximum cable length 600 mm

## Slide 21
maksym.protsenko@cern.ch
Варианты симметричных линий
экран h=50 мкм
прокладка h=50 мкм, ε = 1,75
(h эфф =70 мкм; εэфф = 2,25)
экран h=50 мкм
прокладка h=75 мкм, ε = 1,75
Chart: Ширина проводников, мм
| 0.5 | 0.45 | 0.4 | 0.3500000000000002 | 0.30000000000000021
Зависимость импеданса от ширины проводников | 16.2 | 17.7 | 19.5 | 21.7 | 24.4
экран h=50 мкм
прокладка h=50 мкм, ε = 1,75
(h эфф =120 мкм; εэфф = 2,15)
экран h=50 мкм
прокладка h=75 мкм, ε = 1,75
прокладка h=50 мкм, ε = 1,75
прокладка h=50 мкм, ε = 1,75
Chart: Ширина проводников, мм
| 0.5 | 0.45 | 0.4 | 0.35000000000000031 | 0.30000000000000032
Зависимость импеданса от ширины проводников | 26 | 28.2 | 30.8 | 33.9 | 37.7
экран h=50 мкм
прокладка h=50 мкм, ε = 1,75
(h эфф =195 мкм; εэфф = 1,95)
экран h=50 мкм
прокладка h=75 мкм, ε = 1,75
2 прокладки h=75+50 мкм,
ε = 1,75
2 прокладки h=75+50 мкм,
ε = 1,75
Chart: Ширина проводников, мм
| 0.5 | 0.45 | 0.4 | 0.35000000000000026 | 0.30000000000000027
Зависимость импеданса от ширины проводников | 39 | 41.8 | 45.2 | 49.2 | 53.9

## Slide 22
1.
2.
Measurements | HV, V | Center 238Pu , ch. ADC | Δ, ch. ADC | , %
1. FE – board + Si det (32 p+ strips) | 60 | 763 | 23 | 3,01
2. FE – board + polyimide cable + Si det (32 p+ strips) | 60 | 740 |  | 
Measurements | HV, V | Center 238Pu , ch. ADC | Δ, ch. ADC | 
1. FE – board + Si det (32 p+ strips) | 60 | 763 | 23 | 3,01
2. FE – board + polyimide cable + Si det (32 p+ strips) | 60 | 740 |  | 
Measurement of the attenuation of α-signal in a polyimide cable without vacuum
The signal attenuation with polyimide cable (600 mm lenght or 1200■) is 3%

## Slide 23: General conditions
Luminosity: L=1,2x1032 cm-2 *s-1 ;
1 p-p interaction per 3 bunch crossing;
Expected event rate: 4*106 event per second;
Time between bunch crossing ≈ 70 ns;
At =24 GeV average particle multiplicities ≈ 36 (13,5 – charged, 22,5 –neutral);
π mesons (+, -, 0) 4.6, 3.9, 4.8; K mesons (+, -, 0) 0.4, 0.3, 0.7.
Fig.1The di-muon invariant mass distribution
Fig.2 Distributions of the muon transverse momentum from
the DY events for different angular intervals.
Upper: left- all angles; right - 35o ÷145o
Bottom: left – 3o ÷35o ; right - 0o ÷3o .
[From Letter of Intent]

## Slide 24
End Cap |  |  |  |  | 
 | Number of Si-DSSD (63x63)mm on the end cap | Number of Si –MAPS (15x30)mm on the end cap |  |  | Area, m2
1 end cap - MAPS | 38 | 38 |  |  | 0,017
2 end cap – MAPS | 97 | 97 |  |  | 0,043
3 end cap – MAPS | 160 | 160 |  |  | 0,072
4 end cap – DSSD | 28 |  |  |  | 0,113
5 end cap – DSSD | 41 |  |  |  | 0,164
6 end cap – DSSD | 56 |  |  |  | 0,225
7 end cap – DSSD | 73 |  |  |  | 0,29
 | Total DSSD = 198 det x 2 = 396 det |  |  |  | Total MAPS = 0,132 m2 x 2 =0,264 m2
 | Total MAPS = 295 det x 2 = 590 det | Total MAPS = 295 det x 2 = 590 det |  |  | Total DSSD = 0,79 m2 x 2 =1,58 m2