## Slide 1: HybriLIT – key to the high performance computing in JINR
Gheorghe ADAM
LIT JINR & IFIN-HH
(On behalf of the HybriLIT computation team)

## Slide 2
Why HybriLIT ?
HybriLIT Essentials
Instances of High Performance Computing (HPC) on HybriLIT
QDLab – an open science project
Alleviating the Learning Curve of HPC at HybriLIT
Outline

## Slide 3
Why HybriLIT ?
HybriLIT Essentials
Instances of High Performance Computing (HPC) on HybriLIT
QDLab – an open science project
Alleviating the Learning Curve of HPC at HybriLIT
Outline

## Slide 4
A Checkpoint List (1)
The LIT expertise qualifies it as the JINR developer of general purpose computing facilities devoted to the solution of computing intensive tasks in the Institute.
Two inner basic constraints: The implementation of specific computing facilities follows from the approved JINR scientific projects and is financed from the JINR budget.
Hardware vs. software costs: The expenses within the famous 20/80 ratio characterizing the hardware/software costs have mainly to be restricted to the hardware costs.
The external factor: the practical decisions taken by the LIT management follow the world wide trends in the IT field.

## Slide 5
A Checkpoint List (2)
Building blocks of HybriLIT are the multi-core processors, CPU many-core coprocessors, GPU accelerators and modules of such elementary structures implemented into blades/servers.
The evolution of the TOP 500 lists points to the gradual shift of the high performance computing (HPC) facilities from the monolithic expensive HPC cluster structures to cheaper modular heterogeneous HPC cluster structures.
The culture created in LIT in connection to the Tier-2 and Tier-1 site implementations (as among the most effective within WLCG) facilitates the addition of new facilities on the LIT premises based on the existing background and traditions.

## Slide 6
A Checkpoint List (3)
The HybriLIT philosophy involves three main points:
  gradual development of a modular heterogeneous computing cluster devoted to HPC in JINR and JINR Member States and taking advantage of the already created IT infrastructure;
  prioritization of acquisitions to hardware modules which ensure the highest possible enhancement of the computing resources;
  optimization based on in-house solutions.

## Slide 7
• Purpose: The HybriLIT can be characterized as a modular heterogeneous HPC complex answering to three basic tasks:
● ● Task 1: Design and implementation of parallel software for computing intensive research;
● ● Task 2: Porting to the cluster open software packages and numerical libraries which are already tuned for hybrid architectures;
● ● Task 3: Development of new mathematical methods and parallel algorithms adapted to heterogeneous architectures.
• Implementation: Is done as the HPC component of the Multifunctional Information and Computing Complex (MICC), in train to be developed in LIT as a basic JINR facility.
What Is HybriLIT

## Slide 8
Why HybriLIT ?
HybriLIT Essentials
Instances of High Performance Computing (HPC) on HybriLIT
QDLab – an open science project
Alleviating the Learning Curve of HPC at HybriLIT
Outline

## Slide 9
HybriLIT Overview
# of CPU cores | 252 | # of nodes involving CPU | 10
# of GPU cores | 77184 | # of nodes involving GPU accelerators | 8
# of MIC cores | 182 | # of nodes involving CPU co-processors | 2
Total RAM | 2.4 TB | InfiniBand | 16x FDR 56 Gbps
Total HDD | 55.2 TB | Ethernet | 10 Gbps
Peak performance in single precision floating point arithmetic | 142 TFLOPS | Peak performance in double precision floating point arithmetic | 50 TFLOPS
⃦ Power consumption: 8.29 kW ⃦ Energy efficiency: 4.56 GFlops/W ⃦ Peak power demand: 10 kW |  |  | 
Cluster State by end of June 2016

## Slide 10
System Resources
SLURM
(workload manager)
NFS
(file system)
EOS
(file system)
CernVM-FS
(Virtual Software Appliance)
OS: Scientific Linux 6.7
Nano RAMFS
(bootloader Linux)
Software for parallel computing:
OpenMPI 1.6.5, 1.8.1
CUDA 5.5, 6.0, 6.5, 7.0, 7.5
GNU 4.4.7, 4.8.4, 4.9.3
Intel Parallel Studio XE 2016
PGI 15.3
HybriLIT web-site
http://hybrilit.jinr.ru/
GitLab
https://gitlab-hybrilit.jinr.ru
Indico
http://indico-hybrilit.jinr.ru
HybriLIT user support
https://pm.jinr.ru/projects/hybrilit-user-support
Monitoring
https://stat-hlit.jinr.ru/
MODULES
FreeIPA
(identity manager solution)
HybriLIT
Overview
Software and Information Environment
On-line Information for Users

## Slide 11
Operation System: Scientific Linux 6.7 [will soon migrate to 7.x]
Storage: NFS4, EOS 4.0.26, CVMFS 2.2.3
NFS (Network File System) — network file system provides access to files located on a remote server using the nfs protocol;
EOS — CERN-developed distributed file system provides remote access via the xroot protocol for integrating heterogeneous clusters of this type;
CernVM-FS (CERN Virtual Machine File System) — file system enabling extension of the software library HybriLIT by adding the ability to use open source CERN software.
Managing environment variables: MODULE 3.2.10
Package designed for the control of the configuration of the environment variables in a command shell to run different versions of an application or different applications.
The main commands module add and module rm allow the user to change at will the environment variables defining his/her personal options on the needed OS resources.
Task Scheduler: SLURM 16.05
HybriLIT:
Resources

## Slide 12
Specific requirements for the efficient system administration emerge from the modular expandable structure of the cluster.
The configuration expansion has to meet three basic needs enabling scalability and high fault tolerance:
Dynamic cluster extension in the future by allowing quick add of new computing nodes to the structure of the cluster;
Possibility of simultaneous software changes or upgrades at all computing nodes;
Quick setup of nodes, including errors after reboot.
The fulfillment of these needs was secured by an in-house extension of the network boot method *.
This is a small image interface, called nanoramfs. It includes commands of network settings applicable for each class of blades of the cluster. It is downloaded during the load of the core operation system.
Nanoramfs is located on the central server of the cluster and it carries out unambiguous identification of every required blade.
As soon as the identification procedure is terminated, the current image of ramfs is exported to the corresponding blade.
* Pfister Gregory. "In Search of Clusters" (The ongoing battle in lowly parallel computing (2nd edition)). Prentice Hall, 1997
Efficient System Administration:
Nanoramfs

## Slide 13
Efficient System Administration:
CVMFS: network access to the CERN repository (1)
The operational CVMFS interface implemented at HybriLIT has two main characteristics:
The unused 32 Gb SSD storage at each node is reserved for CVMFS packages;
Dedicated extension of MODULES environment.
hybrilit
cern
Task with ID 2447 uses blade02 by CUDA 7.5
CUDA 7.5
ROOT
Task with ID 2448 uses blade04 by ROOT
CERN Virtual Machine File System

## Slide 14
Efficient System Administration:
CVMFS: network access to the CERN repository (1)
The operational CVMFS interface implemented at HybriLIT has two main characteristics:
The unused 32 Gb SSD storage at each node is reserved for CVMFS packages;
Dedicated extension of MODULES environment.
hybrilit
cern
Task with ID 2447 uses blade02 by CUDA 7.5
CUDA 7.5
ROOT
Task with ID 2448 uses blade04 by ROOT
CERN Virtual Machine File System
The 32 Gb capacity ssd storage available at each compute node is used for CVMFS packages

## Slide 15
MODULES: CVMFS devoted newly added modules
hlit/opencv/2.4.9 hlit/cuda/5.5 hlit/fairsoft/nov15
hlit/openmpi/1.6.5 hlit/cuda/6.0 hlit/gcc/4.8.4
hlit/openmpi/1.8.1 hlit/cuda/6.5 hlit/gcc/4.9.3
hlit/magma/2.0.0 hlit/cuda/6.5 hlit/java/jdk-1.6.0_45
hlit/scotch/6.0.4 hlit/cuda/7.0 hlit/java/jdk-1.7.0_60
hlit/zeromq/4.1.3 hlit/cuda/7.5 hlit/java/jdk-1.8.0_05
hlit/zyre/1.1.0 hlit/czmq/3.0.2
… and so on for Hybrilit own modules …
[user@hydra] module avail
Efficient System Administration:
CVMFS: network access to the CERN repository (2)

## Slide 16
- SLURM (Simple Linux Utility for Resource Management) – a resource manager and task scheduler for computing clusters, defines the available computing nodes.
- SLURM queues up the tasks and manages the overall resource utilization. Apart from the monitoring of the parallel tasks, SLURM distributes the load on the selected nodes.
- Scheduler settings allow SLURM to allocate compute nodes (queues). The table below shows the types of queues, number of nodes in the queue and characteristics of the nodes.
interactive* | cpu | gpu | phi | gpuK80 | long
Number of Nodes |  |  |  |  | 
1 | 9 | 3 | 1 | 3 | 1
Node Features |  |  |  |  | 
2x Intel Xeon E5-2695 v2 NVIDIA K20X Intel Xeon Phi 5110P RAM 128 Gb** | 2x Intel Xeon E5-2695 v2 RAM 128 Gb** | 2x Intel Xeon E5-2695 v2 3x NVIDIA K40 RAM 128 Gb** | 2x Intel Xeon E5-2695 v2 2x Intel Xeon Phi 7120P RAM 128 Gb** | 2x Intel Xeon E5-2695 v3 2x NVIDIA K80, RAM 512 Gb** 2x Intel Xeon E5-2695 v3 4x NVIDIA K80, RAM 512 Gb** | 2x Intel Xeon E5-2695 v2 3x NVIDIA K40 RAM 128 Gb**
* Default queue
** RAM 128 Gb: Default vendor offers; RAM 512 Gb: Customized values
Task Scheduler: SLURM 16.05

## Slide 17
The table shows the supported technologies of parallel programming, implementation, and compilers for C/C++, Fortran
Software Support:
Installed packages for application development
MPI |  | OpenMP |  |  | CUDA | OpenCL
Intel MPI | OpenMPI | GNU | Intel OpenMP | PGI | NVIDIA | NVIDIA
mpiicc mpiicpc mpiifort | mpicc mpicxx mpif77/mpif90 | gcc g++ g77, gfortran | icc icpc ifort | pgcc pgc++ pgf77/pgf90 | nvcc | nvcc

## Slide 18
Package | Version | Instruction for connecting
GNU gcc, g++, g77, gfortran | 4.4.7 | Default
 | 4.8.4 | module add hlit/gcc/4.8.4
 | 4.9.3 | module add hlit/gcc/4.9.3
Intel icc, icpc, ifort | 16.0.1 | module add intel-2016.1.150
Python | 2.7.11 | Default
Java | 1.6.0 | module add hlit/java/jdk-1.6.0_45
 | 1.7.0 | Default
 | 1.8.0 | module add hlit/java/jdk-1.8.0_05
OpenMPI mpicc, mpicxx, mpif77/mpif90 | 1.6.5 | module add hlit/openmpi/1.6.5
 | 1.8.1 | module add hlit/openmpi/1.8.1
Intel MPI mpiicc, mpiicpc, mpiifort | 16.0.1 | module add intel-2016.1.150
CUDA nvcc | 5.5 | module add hlit/cuda/5.5
 | 6.0 | module add hlit/cuda/6.0
 | 6.5 | module add hlit/cuda/6.5
 | 7.0 | module add hlit/cuda/7.0
 | 7.5 | module add hlit/cuda/7.5
PGI pgcc, pgc++, pgf77/pgf90 | 15.3 | module add pgi-2015.15.3
Software Support:
Packages, versions, instructions for connecting

## Slide 19
PANDAROOT 15.07 – Software package (Panda) for FAIRSOFT & FAIRROOT (https://panda.gsi.de/);
MPD 15.07 – Software package (JINR) for MPDROOT & BMNROOT (http://mpd.jinr.ru/dr/ ).
Package | Version | Instruction for connecting
FAIRROOT | 15.07 | module add hlit/fairroot/v15.07a_nov15
FAIRSOFT | 15.07 | module add hlit/fairsoft/nov15
PANDAROOT | 15.07 | module add hlit/pandaroot/jan16-v15.07a_nov15
MPD | 15.07 | module hlit/mpd/20160205-v15.07a_nov15
Software Support:
Software support of large scale experiments

## Slide 20
magma 2.0.0 – Matrix Algebra on GPU and Multicore Architectures (http://icl.cs.utk.edu/magma/);
scotch 6.0.4 – software package for graph and mesh/hypergraph partitioning, graph clustering, and sparse matrix ordering (http://scotch.gforge.inria.fr/);
zeromq 4.1.3 – an intelligent transport layer for distributed apps (http://zeromq.org/);
zyre 1.1.0 – an open-source framework for proximity-based peer-to-peer applications (https://github.com/zeromq/zyre);
czmq 3.0.2 –C/C++ support for ZeroMQ (https://github.com/zeromq/czmq).
Package | Version | Instruction for connecting
magma | 2.0.0 | module add hlit/magma/2.0.0
scotch | 6.0.4 | module add hlit/scotch/6.0.4
zeromq | 4.1.3 | module add hlit/zeromq/4.1.3
zyre | 1.1.0 | module add hlit/zyre/1.1.0
czmq | 3.0.2 | module add hlit/czmq/3.0.2
Software Support:
Specialized libraries and packages

## Slide 21
– CMake is an open-source, cross-platform family of tools designed to build, test and package software.
– CMake is used to control the software compilation process using simple platform and compiler independent configuration files, and generate native makefiles and workspaces that can be used in the compiler environment of your choice: https://cmake.org/
The following versions are installed on the cluster:
Package | Version | Instruction for connecting
CMAKE | 2.8.12 | Default
 | 3.4.1 | module add hlit/cmake/3.4.1
Software Support:
CMake

## Slide 22
Why HybriLIT ?
HybriLIT Essentials
Instances of High Performance Computing (HPC) on HybriLIT
QDLab – an open science project
Alleviating the Learning Curve of HPC at HybriLIT
Outline

## Slide 23
HybriLIT Enables Implementation of Efficient Numerical Methods for Hardly Solvable Problems
An instance: The Asynchronous Differential Evolution Method (ADE) for the numerical investigation of Multiparametric Physical Models using global optimization.
The problem:
Find ,
where the function may be: non-differentiable, non-continuous, multi-modal.
The differential evolution method (DE), advocated by its authors (R. Storn & K. Price, 1995) to require few control variables, to be robust, easy to use and to lend itself very well to parallel computation, has the drawback that the generation of new variations is hindered by the slowest vector.
ADE innovations:
• asynchronicity
• restart to get out from a fake minimum (ADE-R)
• directionality of the search by taking into account pair correlations (ADE-D)
- HybriLIT code implementations have been done for two different physical problems.
Жабицкая, Е.И., Жабицкий, М.В., Математическое моделирование, 2012, т. 24, No. 12, c. 33–37;
Zhabitskaya, E.I., Zhabitsky, M.V., LNCS 7125, Springer Berlin Heidelberg, 2012, pp. 328–333

## Slide 24
Disregarding fluctuations
Including fluctuations
ADE-SFF Structural Analysis of Vesicular Systems
Modeling the structure of poly-dispersed lipid DMPC (1,2-dimyristoyl-sn-glycero-3-phosphocholine) vesicles solvated in 40% sucrose solution. Analysis of small-angle scattering of synchrotron radiation data used the method of Separate Form Factors (SFF), modified in order to include the fluctuations of the lipid bilayers. The fitting of the parameters responsible of the vesicular structures was based on the ADE algorithm.
E.I. Zhabitskaya (LIT Seminar, April 2016)

## Slide 25
Speedup of Multithreaded ADE on HybriLIT
Linear ADE-R speed-up is observed up to
The Rosenbrock problem (D = 10)
Method ADE-R (Npinit = 10, k = 2).
Averaged over 100 runs for each method.
Reliability 100% for both methods.
E.I. Zhabitskaya (LIT Seminar, April 2016)

## Slide 26
Computer time vs number of processes and discretization N. Calculations on the HybriLIT cluster of the microscopic OP for 6He+28Si at 50 Mev/Nucleon.
Most recent results of analysis of elastic scattering and fragmentation processes of 10Be+12C from [Phys. Rev. C 91 (2015) 034606]
V.K. Lukyanov, D.N. Kadrev, E.V. Zemlyanaya, K. Spasova, K.V. Lukyanov, A.N. Antonov, M.K. Gaidarov, PRC 91, 034606 (2015)
Hybrid Optical Potential Description of Elastic Scattering and Fragmentation Processes

## Slide 27
K.V. Lukyanov et al., EXON-2014, Publ. in the Conference Proceedings (2015)
Optical potential computations and comparison with experimental data of total interaction cross-sections of the exotic nuclei 6He and 8,9Li with different nuclei over a large range of energies and masses
Hybrid Optical Potential Computation of Total Interaction Cross-Sections of Exotic Nuclei

## Slide 28
The boundary value problem of the polaron model was formulated and solved using our MPI/C++ code.
The comparison of numerical outputs with experimental data (see figures) has shown that the developed model consistently describes the dynamics of the electron photoemission in water under the laser radiation in the ultra-violet range.
• В.Д. Лахно, А.В. Волохова, Е.В. Земляная, И.В. Амирханов, И.В. Пузынин, Т.П. Пузынина. Поверхность, 1, 82-87, 2015
• E. V. Zemlyanaya, A. V. Volokhova, V. D. Lakhno, I. V. Amirkhanov, I. V. Puzynin, T. P. Puzynina, V. S. Rikhvitskiy, P. Kh. Atanasova, AIP Conf. Proc. 1684, 100006 (2015); http://dx.doi.org/10.1063/1.4934343
Dynamical model of the hydrated electron (polaron)
Efficiency of
Parallel Optimization
The number of serial arithmetic operations at the stage 2 of the above algorithm is growing proportionally to P, i.e., extremely high acceleration of calculations on multi-processor systems is not available.
Maximal acceleration (10 times) is achieved in the case of 12 parallel processes on multi-CPU systems CICC and HybriLIT, and the 4-time speed up is available on a 4-core one-CPU system.

## Slide 29
Optimization and Design of an Ion Source Cryogenic Cell
Alexander Ayriyan, Jan Busa Jr., Eugeny E. Donets, Hovik Grigorian, Jan Pribis, Applied Thermal Engineering (2016), vol. 94, pp. 151–158, doi:10.1016/j.applthermaleng.2015.10.095
Simulation of the thermal behaviour of a multi-cylindrical device with a non-trivial design area and nonlinear thermodynamic properties of materials at cryogenic temperatures.
The model describes the cryogenic cell designed for pulse feeding of working gases in the chamber of a source generating multiply charged ions.
The mode of operation of the cryogenic cell asks for periodic valve opening and closing for injection of a gaseous substance in the millisecond range.
The simulations unveiled the occurrence of a transient regime of the thermal behaviour , with an initialization time of about 5-10 seconds.
The figures above point to various instances of the surface temperature evolution (depth z = 0).
The figure at left points the speed up of the OpenCL GPU parallel algorithm.
The noticed fracture was identified to come from the change of the information flow caused by RAM limitations of the K40 setup.

## Slide 30
Standing Wave Solutions Corresponding to the Cavity
Resonances in BSCCO Intrinsic Josephson Junctions
film_ef.avi
Ivan Hristov, Radoslava Hristova, Stefka Dimova Sofia University, Bulgaria / LIT, JINR, May 26, 2016 Seminar in LIT-JINR
Hybrid MPI+OpenMP Parallelization
of a Leapfrog Algorithm for Solving Systems of 2D Sine-Gordon Equations
Computational challenges in solving this system:
Discretization of the 2D domain may ask for
106–108 mesh points.
Stable integration scheme with respect to the time variable depends on problem parameters and may ask for 108–109 time steps.
The Intrinsic Josephson Junctions in BSCCO crystals (IJJ-BSCO) are a strong source of THz radiation.
The phase dynamics of the IJJ-BSCO is described by a system of perturbed 2D Sine-Gordon equations.
HybriLIT
Intel Xeon
E5-2695 v2
IICT-BAS
Intel Xeon
X5560
IICT-BAS
Intel Xeon
X5560
film_phasei

## Slide 31
Standing Wave Solutions Corresponding to the Cavity
Resonances in BSCCO Intrinsic Josephson Junctions
Ivan Hristov, Radoslava Hristova, Stefka Dimova Sofia University, Bulgaria / LIT, JINR, May 26, 2016 Seminar in LIT-JINR
Hybrid MPI+OpenMP Parallelization
of a Leapfrog Algorithm for Solving Systems of 2D Sine-Gordon Equations
Computational challenges in solving this system:
Discretization of the 2D domain may ask for
106–108 mesh points.
Stable integration scheme with respect to the time variable depends on problem parameters and may ask for 108–109 time steps.
The Intrinsic Josephson Junctions in BSCCO crystals (IJJ-BSCO) are a strong source of THz radiation.
The phase dynamics of the IJJ-BSCO is described by a system of perturbed 2D Sine-Gordon equations.
HybriLIT
Intel Xeon
E5-2695 v2
IICT-BAS
Intel Xeon
X5560
IICT-BAS
Intel Xeon
X5560

## Slide 32
Acceleration dependence on the programming paradigm and code length.
OpenCL and CUDA using a same framework (local group of 512 threads and 100 decoders working in parallel) yield comparable results.
Comparison with CPU code using C++ compiler is done under use of a single Intel Xeon E5-2695v3 core (with O3 optimization).
Time was measured for 10 000 decoded code words at Eb/N0 =2dB.
Performance Evaluation of Parallel Processing in a Case Study of Low Density Parity Check (LDPC) Codes for Error Corrections
OpenCL programing model
CUDA programing model
Benchmarks were conducted on the NASA CCSDS (256,128) standard and its photographically expanded derivations. Run on HybriLIT NVIDIA Tesla K80 (Kepler G210 architecture).
Acceleration dependence on the local group size
Acceleration dependence on the number of decoders working in parallel
Jan Broulim (LIT & TU Prague), Alexander Ayriyan (LIT), in preparation

## Slide 33
Why HybriLIT ?
HybriLIT Essentials
Instances of High Performance Computing (HPC) on HybriLIT
QDLab – an open science project
Alleviating the Learning Curve of HPC at HybriLIT
Outline

## Slide 34
PD Dr. Alexej I. Streltsov
UNIVERSITÄT HEIDELBERG
Dr. Oksana I. Streltsova
LIT JINR, DUBNA
http://QDlab.org
Many-body theory
of bosons group
Heidelberg, Germany
Heterogeneous Computations
HybriLIT - team

## Slide 35
MultiConfigurational Time Dependent Hartree (for) Bosons
1D-2D-3D: Control on dimensionality by changing the aspect ratio of the trap
BECs of alkaline, alkaline earth, and lanthanoid atoms (7Li, 23Na, 39K, 41K, 85Rb, 87Rb, 133Cs, 52Cr, 40Ca, 84Sr, 86Sr, 88Sr, 174Yb,164Dy, and 168Er)
The interatomic interaction can be widely varied with a magnetic Feshbach resonance… (Greiner Lab at Harvard)
Magneto-optical trap

## Slide 36
Two generic regimes: (i) Non-violent (under-the-barrier) and (ii) Explosive (over-the-barrier)
Highly-non-equilibrium quantum dynamics in trapped systems of ultra-cold atoms and molecules (N=100: sudden displacement of trap and sudden quenches of the repulsion in 2D)
Trap displacement:
Inter-particle repulsion quench is described by the variation of the parameter λ0
O.Streltsova (LIT), O.Alon, L.Cederbaum, A.Streltsov, Phys. Rev. A89, 061602(R) (2014)

## Slide 37
MCTDHB-Lab is a free-for-download cross-platform software working on Mac, Windows and Linux
http://QDlab.org

## Slide 38
Why HybriLIT ?
HybriLIT Essentials
Instances of High Performance Computing (HPC) on HybriLIT
QDLab – an open science project
Alleviating the Learning Curve of HPC at HybriLIT
Outline

## Slide 39
• Need of fundamentally different software implementations able to fully exploit the possibilities opened by the new hardware parallelism.
1. New mathematical methods and algorithms enabling efficient information flow inside the new hardware.
2. Grasp of alternative programming paradigms and programming languages.
3. The evolving hardware-software environment allows solving more sophisticated theoretical models, characterized by newly added features which make them more realistic.
4. The reliable numerical or symbolic-numerical solution of such models asks, in its turn, for the development of new approaches to their solutions.
The hardware – algorithms – software interplay

## Slide 40
• Hardware availability does not guarantee success.
Tough scientific problems cannot be simply solved by securing access to the most powerful computing facilities.
• New approaches to solution may be asked to secure:
— inheritance of the genuine algebraic properties of the model under discretization;
— reduction of the computational complexity;
— avoidance of artefacts coming from the finite precision of the floating point representation of the machine numbers, which may result in modifications of fundamental well established features over the field of the real numbers.
Reliance on new mathematics

## Slide 41
System Resources
SLURM
(workload manager)
NFS
(file system)
EOS
(file system)
CernVM-FS
(Virtual Software Appliance)
OS: Scientific Linux 6.7
Nano RAMFS
(bootloader Linux)
Software for parallel computing:
OpenMPI 1.6.5, 1.8.1
CUDA 5.5, 6.0, 6.5, 7.0, 7.5
GNU 4.4.7, 4.8.4, 4.9.3
Intel Parallel Studio XE 2016
PGI 15.3
HybriLIT web-site
http://hybrilit.jinr.ru/
GitLab
https://gitlab-hybrilit.jinr.ru
Indico
http://indico-hybrilit.jinr.ru
HybriLIT user support
https://pm.jinr.ru/projects/hybrilit-user-support
Monitoring
https://stat-hlit.jinr.ru/
MODULES
FreeIPA
(identity manager solution)
HybriLIT
Overview
Software and Information Environment
On-line Information for Users

## Slide 42
Tutorials on the HybriLIT use:
• Frequent tutorials on parallel programming techniques for the institute staff and, under JINR-UC organization, for students and young scientists from JINR Member-States;
• Specialized courses from leading software developers.
Specialized courses and seminars within JINR-organized conferences and schools.
HybriLIT-Indico site mentions, mostly for 2015 and 2016: 21 tutorials (1 in 2014, 12 in 2015, 8 in 2016); 16 specialized meetings; 18 series of lectures on parallel programming techniques, etc.
Participants (over 300, mostly young) from: JINR, Austria, Germany, India, Ireland, Japan, Romania, Russia, Slovakia, Ukraine, etc.
HybriLIT: User training

## Slide 43
Task Coordinators:
Peter V. Zrelov; Gheorghe Adam; Dmitry V. Podgainy; Oxana I. Streltsova
System Administrators:
Dmitry V. Belyakov; Mikhail A. Matveev; Martin Vala
IT & Software Development:
Alexandr Ayriyan; Evgeny I. Alexandrov; Maxim V. Bashashin;
Tatiana F. Sapozhnikova; Elena V. Zemlyanaya; Maxim I. Zuev
General Project Support:
Margarit H. Kirakosyan; Shushanik Torosyan; Tatiana N. Zaikina
HybriLIT Computation Team
http://hlit.jinr.ru/

## Slide 44
The heterogeneous HPC cluster HybriLIT is being developed in LIT-JINR as part of the JINR Multifunctional Information and Computing Complex (MICC)
It is mainly devoted to the solution of computer intensive tasks emerging from the large scale JINR scientific projects, in particular the flagman NICA-MPD project
The created HybriLIT information-software environment provides a solid basis for smooth further extensions of the cluster with new compute modules
The modern solutions adopted for the user support combine on-line information with dedicated tutorials, master classes, lectures, etc.
The successful solution of several complex scientific tasks gives optimistic hope on the future of the HybriLIT cluster
Conclusions

## Slide 45
Thank you for your attention !
Join HybriLIT!