## Slide 1
2019 News in power supply HV/LV and Digital Readout Electronics
Gianni Di Maio
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
JINR 3rd Collaboration meeting of the MPD and BM@N NICA Facility, April 17th 2019

## Slide 2
Outline and activity
Company Overview
Network of Companies
LHC & CAEN
The EASY System
Summary about CAEN HV/LV power supply
Summary about CAEN Digital Readout Electronic
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 3
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Founded in 1979, for more than 40 years CAEN has been providing Scientists and Engineers with the most advanced electronic instrumentation designed for radiation & low light detectors
Strong of an extremely close collaboration with the world major research laboratories CAEN is proud to produce the best tools for:
  High Energy Physics
  Nuclear Physics
  Neutrino Physics
  Astrophysics
  Dark Matter Investigation
  Educational
  Medical Applications
  Homeland Security
  Industrial Applications
  and more …
Introduction
Notes: 3

## Slide 4
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
CAEN SpA Headquarters Viareggio, Italy
CAEN Gmbh, Germany
CAEN Technologies Inc., USA
Notes: 4

## Slide 5
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Worldwide sales network offices in Italy, Germany, USA, Distributors in more than 30 countries.
Portfolio: > 5000 customers Customers Include all world leading research centres as:
Europe: CERN,JINR,INFN, CEA, CNRS; GSI, ESO, ISIS, Ganil, PSI, …
USA: FNAL, SLAC, Los Alamos, BNL, Jlab, …
Asia: J-Park, KEK, Riken, IHEP, TIFR, …
Africa: iThemba Labs, …
And private companies: GE, Siemens, SAIC, L3, Raytheon, Lockheed, Bosch…
Global Coverage
Notes: 5

## Slide 6
More than 40 Years of activity in Physics Research allow CAEN the right way to approach and collaborate with the big projects thanks to our:
R&D Division(50 high level Physicists and Engineers at the forefront of technology
  Catalog Products
  Customization of catalog models
  Custom projects
Production Division
Capability: 500 complex modules/month
Test Division
Experienced group of 20 engineers
Maintenance Division (15 engineers)
Long Term Maintenance Contract (CERN 10 years and more components stock)
CAEN is ISO 9001 certified since 1998
CAEN Key Strengths
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Notes: 6

## Slide 7
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Network of Companies
Core business: Electronic Instrumentation for physics experiments (worldleader)
Spin-off activities:
> RFID (2003),
> CAENels (2010)
> CAENqS (2012)
> CAEN SyS (2016)
Total Employees: 154
Notes: 7

## Slide 8: LHC & CAEN: a decade of Research & Development
The involvement of CAEN in LHC was in the design, manufacture and supply of HV/LV power supplies and readout electronic to many sub detectors of the 4 Experiments
The first phase of research & development began in the second half of the 90s and ended around 2005 to 2008
The challenges faced and overcome:
  The ” hostile environment”
  The harmonization of the different user requirements to be implemented in a consistent line of products
  Special requests of some users (Alice TOF; Atlas Trigger; CMS DT, ECAL e Tracker)
  CERN preselected CAEN as reliable electronic supplier

## Slide 9: The EASY System for LHC (CERN)
The EASY system is thus the end product of a long period of research, and we can say that CAEN was the only company willing to invest heavily in this particular area
The EASY system has proved successful, and has been adopted in a large extent, especially in Atlas and CMS
The ability to manage LV modules also allowed the company to expand its offerings beyond traditional HV power supplies
Main EASY System features
21 slots per crate
3 kW Maximum Output Power
Magnetic field tolerance: 5 kGauss
Radiation tolerance: 5*1010 p/cm2 TD
2*1011 n/cm2 TD
15 kRad TID

## Slide 10
1998 – 2008
SYNERGY for SUCCESS
CAEN has received the ”CMS Crystal Award of the year 2009” for the development and production of the power system for the CMS Tracker.
  Detector subdivided into 1994 Power groups
  HV (0600V) for silicon strip detector
  LV (1.25V - 2.5V) for FE electronics
  Itot > 15 kA
  139 crates / 29 racks / 1200 Power Supply Units

## Slide 11: Modules EASY- 1
and A4601F / A4601H / A4602 / A4603 – special boards for CMS Tracker/Pixel

## Slide 12: Moduli EASY - 2

## Slide 13: LHC & CAEN: some numbers
During the LHC production phase:
  8.500 electronic modules build of:
    210.000 PCBs
    28.000.000 components

## Slide 14
High Voltage & Low Voltage Power Supplies
  Multi-Channel CAEN Systems
  Multi-Channel NIM and VME Modules
  Stand-alone Power Supplies
  PCB mountable HV DC-DC converters
Signal Conditioning, Read-out Electronics & Emulation
  Waveform Digitizers & Digital Pulse Processing
  Digital MCA and instrumented PMT bases
  Digital Detector Emulators
  NIM and VME traditional electronics
  Preamplifiers
Powered Crates and Chassis
  Low Ripple Linear NIM powered Crates
  New Hi-End VME64/VME64x Crates
  Educational Kit
  Partnership
CAEN catalog includes more than 300 product categories (~1000 items)
CAEN Catalog Products
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 15
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Power Supplies
CAEN Power Supplies: a perfect blend of
tradition and innovation
Notes: 15

## Slide 16
Universal Multichannel System

## Slide 17
System Philosophy
Modularity
  Chassis: SY4527, SY5527, SY4527LC, SY5527LC
  CPU Units: Basic, Advanced, Full
  Power Units: Primary, Boosters
  Accessories: LCD Touchscreen, Wi-Fi, Advanced SW
  Connectivity
    Control based on new CPU modules either Remote via Ethernet and Wi-Fi or Local via touchscreen LCD
  Usability
    New Software tools have been designed to set and monitor all the parameters. Advanced features for Alarming, Logging and Scripting
Compatibility
    The new backplane is fully compatible with SY1527/2527 HV/LV Boards and Branch Controllers

## Slide 18
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Fully equipped experiment version
19" wide, 8U-high Euro-mechanics rack; depth: 720 mm, weight : 13kg
16 slots to house boards, distributors and branch controller
Communications via Gigabit Ethernet and via Wi-Fi (optional)
Local control via 10.4" color touchscreen LCD (optional)
Fast, accurate setting and monitoring of channel parameters
Modular and expandable power supply (up to 4 kW)
Forced air cooling
SY4527 Highlights
Notes: 18

## Slide 19
Small scale experiment and laboratory version
19" wide, 4U-high Euro-mechanics rack; depth: 700 mm
6 slots to house boards, distributors and branch controller
Communications via Gigabit Ethernet and via Wi-Fi (optional)
Local control via 5.7" colour touchscreen LCD (optional)
Fast, accurate setting and monitoring of channel parameters
Modular and expandable power supply (up to 1800 W)
Forced air cooling
SY5527 Highlights

## Slide 20
Universal Multichannel Systems - New Multichannel Boards
CAEN introduces a large number of completely new families of both Low Voltage and High Voltage Multichannel Power Supply Boards for the new Universal Multichannel Systems
Many New and Coming Soon ordering options ranging from 4 V up to 12 kV have been introduced in the new 2016/2017 Catalog!
The new board families join the already wide selection of LV and HV power supplies extending the CAEN catalog to fit well any application in Nuclear and High Energy Physics
Extended modular choices: 6, 8, 12, 24, 32, 36, 48 channels per board to cope well with any application

## Slide 21
Universal Multichannel Systems - New Multichannel Boards
A new categorization of CAEN Multichannel Power Supply Boards introduced to guide the users in finding the best solution for their applications
The Boards have been divided by:
Maximum Output Voltage
  Low Voltage
  Up to 500 V Family
  Up to 4 kV
  Up to 8 kV
  Up to 15 kV
Channel Grounding
  Common Ground
  Common Floating Return
  Individual Floating Channel
NO DISTRIBUTORS ANYMORE !!!
Channel Architecture
  Independent Channel
  Independent Dual Range Channel
  Board for Specific Application

## Slide 22
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Universal Multichannel Systems - Multichannel Boards
Independent Voltage Sense Lines
Individual Line Drop Recovery (only A151x family)
High Resolution on Voltage set
Voltage Ripple < 5 mVpp
Digital PID control loop (only A251x)
Parallelizable Channels
50 W Max channel output power (only A251x family)
Low Voltage Power Supplies: A151x and A251x
6/8 channel, Up to 15 V, Up to 15 A
Notes: 22

## Slide 23
2 different channel grounding:
  Common Ground (AG5xx)
  Common Floating return (A1539 and A154x)
DB25 Multi pin or SHV coaxial connectors
Available with positive, negative or mixed polarity
1 mV voltage monitor resolution
100 pA current monitor resolution
Low Ripple
Independently programmable channells
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Universal Multichannel Systems - Multichannel Boards
Solution for General Purpose Setups: A1539 and A154x
12/24/32 channel, up to 500 V, 10 mA HV power supply
Notes: 23

## Slide 24
12 independent single and dual range HV channels
Either DB or AMP Multipin connectors
Full floating channels
Individual Enable
Up to 10 nA current set / monitor resolution
Up to 1 mV voltage set / monitor resolution
Specific features for double-side silicon detectors (A151x)
Specific features for APD detectors (A1520P)
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Universal Multichannel Systems - Multichannel Boards
Solution for Silicon Detectors and APDs:
A151x and A1520P
12 channel, up to 500 V, 15 mA HV power supply
Notes: 24

## Slide 25
Same channel density as Distributors, but with all the advantages of independent channels
Settings and safety parameters independently selectable
Up to 500 V, up to 500 uA per channel
SHV coaxial connectors
10 mV Voltage monitor resolution
1 nA Current monitor resolution
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Universal Multichannel Systems - Multichannel Boards
Solution for high density detector arrays: A7040/A7042
48 channel, 100/500 V, 500 uA HV power supply
Notes: 25

## Slide 26
Up to 48 High Voltage independent channels in one single slot board
Same channel density as Distributors, but with all the advantages of independent channels
Settings and safety parameters independently selectable
Radiall 52 pin or SHV coaxial connectors
5 mV Voltage monitor resolution
2 nA Current monitor resolution
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Universal Multichannel Systems - Multichannel Boards
Solution for large PMT Arrays: A7030
12/24/36/48 channel, 3 kV/1 mA (1.5 W max) HV power supply
Notes: 26

## Slide 27
Up to 32 High Voltage, High Power independent channels in one single slot board
Settings and safety parameters independently selectable:
  Output voltage (5 mV set/mon resolution)
  Current limit (1 nA resolution, x10 zoom option available)
  Ramp up/down (1÷500 Volt/sec)
  TRIP time
Up to 3.5 kV, up to 1.5 mA (4 W max) or 3.5 mA (9 W max) per channel
Radiall 52 pin connector
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Universal Multichannel Systems - Multichannel Boards
A7435: 24 channel, 3.5 kV/3.5 mA HV power supply
A7236: 32 channel, 3.5 kV/1.5 mA HV power supply
Solution for High Power and High Resolution
application: A7236 and A7435
Notes: 27

## Slide 28
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Universal Multichannel Systems - Multichannel Boards
Solution for GEM Detectors: A1515/1515TG/A1515QG
A1515: 16 ch 1kV 1 mA/100 uA dual range
TG: 14 HV ch. grouped to power 2 Triple GEM
QG: 16 HV ch. grouped to power 2 Quadruple GEM
Grounding: Each channel floating up to 5 kV
Vmon resolution: 10 mV
Imon res: 1 nA (High range); 100 pA (Low range)
Voltage Ripple: < 15 mV
Individually floating
stacked channels, ideal for multi-layered GEM!
Notes: 28

## Slide 29
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Universal Multichannel Systems - Multichannel Boards
8/16 channels 6/8 kV 20 µA with Independent Enable
8 or 16 channels in one single slot
Individual hardware Enable connector
0÷6 kV or 0÷8 kV output voltage
20 µA maximum output current per channel
Common floating return
Radiall 52 pin or SHV coaxial connectors
10 mV voltage monitor resolution
50 pA current monitor resolution
Ripple: < 5 mVpp
Solution for HPGe and gaseous detectors: A1560H/A1580H
Notes: 29

## Slide 30
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Universal Multichannel Systems - Multichannel Boards
Solution for accelerator or industrial application: A1588
8 channels Bipolar High Voltage Power Supply
Four-quadrant bipolar power supply
± 2 kV @ ± 0.5 mA output ratings
Common floating return
SHV connectors
Voltage ripple of < 10 mVpp
Internal Hardware protections
Excellent long-term output stability
External interlocks (active + passive)
Notes: 30

## Slide 31
VME, NIM and Standalone solution

## Slide 32
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Modular VME power supplies
VME HV Boards Family
V6519, V6533, V6534, V6521, V6521H
Thanks to the GECO2020 control software and the multimaster capabiity of CAEN VME Bridges, CAEN VME HV power supplies become a System:
DAQ and HV in the same VME crate independently controlled!
Overview
6 channels in 1 VME Unit
From 500 to 6 kV, from 20 µA to 3 mA
Common Floating Return
SHV connectors
Voltage ripple < 3 mVpp
Internal Hardware protections
Available with positive, negative or mixed polarity
Notes: 32

## Slide 33
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
NIM-NDT High Voltage Power Supplies
NIM and NDT HV Boards Family
N14xx, NDT14xx and N14xxET
Overview:
4/2/1 channles in 1 NIM Unit
From 500 to 8 kV, from 20 µA to 3 mA
Common Floating Return
SHV connectors
Voltage ripple < 5 mVpp
Internal Hardware protections
Independently selectable channel polarity
Local and Remote control
Now also with Ethernet connection!
2.8’’ color touch screen display (only NDT)
110-220 Vac plug for desktop operation (Only NDT)
Notes: 33

## Slide 34
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Rack-mountable High Voltage Power Supplies
Rack-mountable HV Boards Family
R1419ET, R1470ET, R1471ET, R1471HET
Overview:
4 or 8 channles in 2U, 19’’ rack unit
2.8’’ color touch screen display
110-220 Vac plug for desktop operation
from 500 to 8 kV, from 20 µA to 3 mA
Common Floating Return
SHV connectors
Internal Hardware protections
Independently selectable channel polarity
Local and Remote control (USB/Ethernet)
Notes: 34

## Slide 35
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Desktop High Voltage Power Supplies
Solution for small setups: Desktop HV Boards Families
DT55xxE, DT14xxET, DT547x
Overview:
4 channels in desktop module
from 500 V to 6 kV, from 20 µA to 3 mA (DT55xxE)
from 500 V to 8 kV, from 20 µA to 3 mA (DT14xxET)
Common Floating Return
SHV connectors
Available with positive, negative or mixed polarity
Local and Remote control (USB/Ethernet)
Individual channel enable
2.8’’ color touch screen display (DT14xxET)
110-220 Vac plug for desktop operation (DT14xxET)
Independently selectable channel polarity (DT14xxET)
Notes: 35

## Slide 36
Desktop High Voltage Power Supplies
Single Channel USB Desktop HV Boards Family
DT547x
Overview:
Single Desktop HV channel powered and controlled by USB
Channel Enable/Disable via front panel switch
Available with positive or negative polarity
SHV coaxial output connector
From 500 V to 5 kV, 1 W maximum power
Imon Zoom (x10)
Remote control through USB 2.0
LabVIEW Instrument Driver
High Voltage power supplies now available in a compact, easy and handy device

## Slide 37
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
PCB mountable HV DC-DC converters
PCB High Voltage Power Supply
A7501, A7504, A7505, A7508
Single High Voltage Channel in a PCB mount architecture
Compact package 29x54x16 mm3 (WxLxH)
High Efficiency and low power consumption
Three Models available:
  A7501 (2100 V / 100 μA)
  A7504 (4000 V / 100 μA)
  A7505 (1600 V / 500 μA)
  A7508 (800V / 50 uA)
Analog voltage and current Set/Monitor
Ripple/noise: < 5mVpp typ
Excellent stability
High operating temperature range
PCB Double polarity High Voltage Power Supply
A7560
Stand alone architecture
Compact package 49x49x23 mm3 (WxLxH)
High efficiency ± 6kV/10 µA output ranges
Power requirement: < 500mW @ full power
Ripple/noise: < 10mVpp typ
Setting DAC: 16bit, Monitor ADC: 20bit
Serial Line: USART (TX, RX)
Digital control loop with resident parameters and calibration
Works in magnetic field up to 1 kGauss
Notes: 37

## Slide 38: CAEN and ESO LV Power Supply for ALMA
Design of custom LV Power Supply System for ALMA
8 different voltage channels per System
86 Systems produced
Linear Power Supply
Very low ripple/noise performance
Harsh environmental condition (desert at 5,000 m altitude)
  high reliability
  simplified maintenance
  requirements for vibration, shocks, transportation, earthquake, air pressure, dust
CAEN Custom solutions

## Slide 39
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Modular Fast Pulse Electronics
CAEN Modular Pulse Processing Instrumentation:
from traditional chains to digitization
Notes: 39

## Slide 40
Analog
Traditional readout system
Detector
TDC
Peak
Sensing
Pulse Height
Charge
(Integral)
Counts
Rise Time
ADC
A/D conversion
at end of chain
Energy Spectrum (MCA)
MCS/Rates
Logic
Timing
Filter
Shaping
Amplif
Delay
SCA1
Preamp
Veto
Coinc
Gate,Trg, …
QDC
Scaler
PSD
Digital
Many analog
modules and cables
SCA2
TDC
Arrival
Time
Tref
TAC/TOF
Manual
Setting
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 41
Digital Readout: all-in-one
Detector
Energy Spectrum (MCA)
MCS/ICR
TAC/TOF
TDC
Timing
Filter
Delay
Discr
Scaler
Preamp
FADC
Peak
Sensing
Shaping
early A/D conversion
FPGA
Gate, Veto and
Coincidences
Integral
PHA
QDC
Counts
Time
Double
Integral
Fast/Slow
Logic
Sync
PSD
BLR
BLR
streaming
01100101
Software
Setting

## Slide 42
Digital Acquisition Chain
samples
01100101
Waveform
Recorder
Pulse
Processor
waveforms
s1, s2, …
CPU
events
T,E,S
spectra
Histo
Oscilloscope
Mode
Multi-Parametric
List Mode
Digital
Spectrometer
12334
234
0.55
134567
1034
0.95
234456
34
0.66
345664
2234
0.45
378902
123
0.57
435872
22
0.15
567342
3345
0.17
634652
623
0.88
12334
234
0.55
134567
1034
0.95
234456
34
0.66
345664
2234
0.45
378902
123
0.57
435872
22
0.15
567342
3345
0.17
634652
623
0.88
12334
234
0.55
134567
1034
0.95
234456
34
0.66
345664
2234
0.45
378902
123
0.57
435872
22
0.15
567342
3345
0.17
634652
623
0.88
Configuration &
Monitoring
Post Process,
Event building
Analysis,
Identification
DIGITAL
ANALOG
FADC
10-100 MB/s
100M - 1GB/s
100k-1MB/s
1kB/s
Ext or Self
Trigger
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 43
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Waveform Digitizers
A wide selection of multichannel waveform digitizers:
From 1 to 64 channels
From 62.5 MS/s to 5 GS/s
From 8 to 14 bits
Available in NIM, Desktop, VME
Notes: 43

## Slide 44
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Overview:
VME64/VME64X (16 ch.), NIM (8 ch.) and Desktop (8 ch.) modules
0.5 and 2 Vpp selectable input dynamic range
VME64/VME64X, USB and Optical Link communication interfaces
Multi-board synchronization features
Daisy chain capability
Demo software tools, DPP Control Software, C and LabVIEW libraries
Algorithms for Digital Pulse Processing
    Pulse Height Analysis (DPP-PHA)
    Pulse Shape Discrimination (DPP-PSD)
Waveform Digitizers
730/725 Digitizer Family
14-bit 500/250 MS/s Digitizer
Outstanding performance
Notes: 44

## Slide 45
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Overview:
1024 samples per event
VME64/VME64X (32 ch.), NIM (16 ch.) and Desktop (16 ch.) modules
Special analog inputs for fast trigger
1 Vpp input dynamic range with programmable DC offset
VME64/VME64X, USB and Optical Link communication interfaces
Multi-board synchronization features
16 programmable LVDS I/Os
Daisy chain capability
Demo software tools, C and LabVIEW libraries
Waveform Digitizers
742 Digitizer Family
12-bit 5/2.5/1 GS/s Switched Capacitor Array Digitizer
Based on DRS4 chip (PSI)
Notes: 45

## Slide 46
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Overview:
1024 samples per event
VME64/VME64X (16 ch.), NIM (8 ch.) and Desktop (8 ch.) modules
2.5 Vpp input dynamic range with programmable DC offset
One discriminator per channel with programmable threshold
Adjustable post-trigger delay (up to 1.25 µs @ 3.2 GS/s)
One pulser per channel
On-board charge calculation for fast histogramming
VME64/VME64X, USB and Optical Link communication interfaces
Oscilloscope software tools, C and LabVIEW libraries
Waveform Digitizers
743 Digitizer Family
12-bit 3.2/1.6/0.8/0.4 GS/s Switched Capacitor Array Digitizer
Based on SAMLONG chip
(CEA/IRFU&IN2P3/LAL)
Notes: 46

## Slide 47
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Digitizer Software
Libraries
    CAENComm
    CAENDigitizer
    CAENDPP
Configuration tools
    CAEN Upgrader
    CAEN VME Demo
Readout Software
    WaveDump
    CAENScope
    WaveCatcher
    DPP Control Software
    MC2 Analyzer
CAEN provides a family of software tools to easily configure and control digitizers
Notes: 47

## Slide 48
Digitizer Software
CoMPASS
Multiparametric DAQ Software for Physics Applications
Software for simultaneous DPP acquisition:PHA, PSD, CI, QDC
• Multi-board management
• Synchronization of multiple boards even from different families
• Correlation between different channels
• Simultaneous plot of waveform, energy, time, PSD, and TOF spectra
• Energy calibration
• Digital CFD for fine time stamp interpolation (pico second intrinsic resolution)
• Selectable filters on energy, PSD, and Correlation
• Data can be retrieved offline to make additional filters and analysis
• ROOT format data saving (Coming Soon)
• Add-on for ROOT integration (Coming Soon)

## Slide 49
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Spectroscopy Solutions
CAEN introduces complete Digital Systems for X-ray, Gamma Spectroscopy and other applications
Notes: 49

## Slide 50
Spectroscopy Solutions
DT5780/DT5781
Dual/Quad Digital Multi Channel Analyzer
Overview:
Dual/Quad Digital MCA based on 14 bit 100 MS/s Flash ADC
Suited for high resolution X-ray and Gamma-ray Spectroscopy
Selectable Input Dynamic Range and adjustable Fine Gain
2 channels HV power supply ( ±5 kV/300 µA)
2 DB9 connectors for preamplifier power supply
HV Inhibit input
Features DPP-PHA firmware for energy and time stamp calculation
Digital oscilloscope function for an easy setup and signal monitoring
Live energy spectrum correction based on advanced techniques for pile-up rejection
Counting Rate up to 1 Mcps
USB and Optical Link communication interfaces
Software interface for configuration, acquisition, data plotting and HV management

## Slide 51
Spectroscopy Solutions
MC2 Analyzer (MC2A)
Graphical software tool for digitizers running DPP-PHA firmware
Overview:
Designed for digitizers running DPP-PHA like 724 family or the Dual Digital MCA DT5780.
Complete simultaneous control of different boards
Full setting of all the relevant DPP-PHA parameters and power supplies for DT5780
Advanced mathematical analysis on collected spectra (peak search, background subtraction, peak fitting, etc.)
Provides Energy - Time Stamp lists and histograms in ASCII and ANSI N42.42 format

## Slide 52
Spectroscopy Solutions
DT5790
Dual Digital Acquisition System for Charge Integration and Pulse Shape Discrimination
Overview:
Dual digital acquisition system based on 12-bit 250 MS/s FlashADCs
Suited for detectors based on Organic, Inorganic and Liquid Scintillators
Two HV channels to bias detectors up to ± 4 kV, 3 mA
Two Preamp power connectors ± 12 V, ± 24 V
On line Digital Pulse Processing for Charge Integration and Pulse Shape Discrimination (DPP-PSD)
No dead time due to conversion
Multiple trace digital oscilloscope for an easy setup and signal monitoring
Coincidences & anti coincidences of 2 channels
Windows and Linux, 32 and 64 bit OS supported
C/C++ and LabVIEW libraries for an easy interface to custom DAQ systems
USB and Optical Link communication interfaces

## Slide 53
Spectroscopy Solutions
DT5770
Compact Digital Multichannel Analyzer
A pocket-size, high performance and cost-effective solution for your spectroscopy applications.
• Compact portable 16k Digital MCA
• Suited for high resolution gamma spectroscopy
• Support continuous and pulsed reset preamplifiers
• Software selectable coarse and fine gain
• DB9 connector for preamplifier power supply
• Features PHA firmware for energy calculation
• Different acquisition modes are available: PHA and signal inspector for an easy setup and signal monitoring
• Software adjustable digital shaping filter, baseline restoration
• On-line pile-up rejection and software dead time evaluation
• USB and Ethernet communication interfaces

## Slide 54
Hexagon: Single/Dual 32k Digital MCA
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Fully integrated, digital MCA operating in PHA mode (up to 32k), Time stamped List mode, MCS(*), SCA(*), Multi-PHA(*).
Suitable for HPGe, Si, NaI, CsI, LaBr3, CdTe, CZT and other detectors. Accepts RC and TRP preamps and PMT anode signals.
Embedded Linux (ARM) for unattended acquisition, data logging (SDD), user programmable routines (SDK provided).
Triple range HV: 5kV/20µA (HPGe mode) , 2kV/1mA (PMT mode), 500V/50µA (Si mode) positive/negative.
10/100T Ethernet and USB 2.0 interfaces. OLED Display. Configurable digital I/Os and Sync bus.
Coincidence and Anti-Coincidence mode (e.g. Anti-Compton or Background Active Shields)

## Slide 55
From Digital MCA to Digital Portable Instruments
γstream
Fully stand-alone MCA including high voltage power supply, preamplifier, battery and data-storage on SSD
Embedded computer (ARM based CPU) for unattended operations
Wired and wireless connectivity through USB, Ethernet, Bluetooth and WiFi
Compatible with scintillation detectors using standard 14-pin PMTs
Different acquisition modes available: PHA, PHA with time stamp, MCS, SCA and waves
Software selectable coarse and fine gain
Front panel auxiliary digital I/O connectors for synchronization, external trigger, coincidence/anticoincidence modes, veto. MCS, SCA
γ stream is an active, stand-alone, fully featured MCA tube base for scintillation spectroscopy

## Slide 56
Indoor use
source calibrations
network of detectors for radiation monitoring in buildings, warehouses, and plants
particle physics
medical imaging
homeland security (e.g. airports)
γstream - software
Two different software tools are available according to the needs and applications
MC2 Analyzer on PC
Outdoor use
orphan sources detection
outdoor radiation monitoring
homeland security (e.g. ports)
building materials
geophysics
gas & oil
GammaTOUCH on smartphone

## Slide 57
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Powered Crates
NIM and VME crates also available to fit most of the applications
  Full Sized
  Compact (2-4-8 slot)
  Mixed (Both NIM and VME slots in the same chassis)
Notes: 57

## Slide 58
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Preamplifiers
CAEN Preamplifiers for most application in Particle and Nuclear Physics
Charge Sensitive Preamplifiers
  A422A (1 Channel with Timing)
  A1422 (1, 4, 8 Channels)
  A1422H (Hybrids)
  A1424 (Scintillation Preamplifier)
Wideband Amplifiers
  A1423 (1 Channel, 1.5 GHz Bandwidth)
Fast Charge Amplifiers
  A1425 (1 Channel, fast rise time)
Matched Amplifiers
  A1426 (1 Channel, Zin = 50 Ohm)
    Insensitive to the cable
Notes: 58

## Slide 59
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Digital Detector Emulator
The only synthesizer of random pulses that is also an emulator of radiation detector signals with the possibility to configure the energy and time distribution
Notes: 59

## Slide 60
Digital Detector Emulator
Products line:
DT5800 Desktop Digital Detector Emulator
    DT5800S – Single Channel Version
    DT5800D – Dual Channel Version
NDT6800 NIM/Desktop Digital Detector Emulator
    NDT6800S – Single Channel Version
    NDT6800D – Dual Channel Version
DT5810 Desktop Fast Digital Detector Emulator
    DT5810D – Dual Channel Version
DT4800 Desktop Micro Digital Detector Emulator
    DT6800S – Single Channel Version

## Slide 61
• Sub-ns rise time
• Pulser/Emulator/Function Generator operating modes
• Energy spectrum emulation
• Time distribution emulation
• Custom signal shape emulation
• Pile-up emulation
• Noise and periodic interference emulation
• Baseline drift
• 1 ns/step programmable delay generator
• Correlated signals generation on the two output channels
• Two shape on the same channel for testing the pulse shape discrimination
• Continuous and pulsed reset pre-amplifier emulation
Digital Detector Emulator
DT5810
Fast Digital Detector Emulator

## Slide 62
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Educational Kit
A modern, digital yet flexible platform for teaching the fundamentals of
Statistics & Particles Detection
Notes: 62

## Slide 63
Developed together with the University of Insubria, Como, the Educational Kit is ideal for
Physics teaching, thanks to its extraordinary features
Educational Kit
Highlights
No Need of High Voltage
Multidisciplinary
Control and Analysis Software Included
Educational Notes Included
Proposed Experiences
Poisson Statistics
Gamma Spectrometry
Positron Annihilation
Cosmic Rays
X-Rays

## Slide 64
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
Partnership
Notes: 64

## Slide 65
CAEN & Weeroc
CAEN is the worldwide distributor of the Weeroc ASICs
Weeroc is a spin-off company from Omega laboratory (IN2P3/CNRS, french governmental agency for fundamental research in astrophysics, particle physics and nuclear physics). Weeroc designs and provides analogue and mixed ASICs for industry and research.
Applications:
Medical imaging
Homeland security
Nuclear protection
Scientific instrumentation
Space (launchers and satellites)

## Slide 66
CAEN & Weeroc
CATIROC is a 16-channel front-end ASIC designed to readout photomultiplier tubes (PMTs) in large scale applications such as water Cerenkov experiments
CITIROC is a 32-channel front-end ASIC designed to readout silicon photo-multipliers (SiPM). Used in the A1702/DT5702
MAROC3 is a 64-channel chip designed to readout negative fast input current pulses such as those provided by Multi Anode Photo Multipliers
PETIROC2 is a 32-channel front-end ASIC designed to readout silicon photomultipliers (SiPMs) with both polarities for particle time-of-flight measurement applications
SKIROC2 is a 64-channel front-end ASIC designed to readout silicon PIN diodes
CAEN will also provide an evaluation board based on the DT5550

## Slide 67
A1702/DT5702
32 Channel Silicon Photomultipliers Readout Front-End Board
Provides bias voltage in the range of 20-90 V individually adjustable for each of 32 SiPMs
Amplification and shaping of the SiPMs output pulse on each of 32 channels
Discrimination of shaped signal at configurable level from 0 to 50 SiPMs photo-electrons
Providing basic coincidence of signals from each pair of adjacent even-odd channels
Allows to trigger only on events that happen in coincidence with event in a group of other A1702 (event validation)
Formation of the trigger for digitization of the signal amplitude
Formation of the time stamp with respect to an input reference signal with 1 ns accuracy
Digitization of signal amplitude of all 32 channels
Data buffering
Efficient back-end communication based on Ethernet standard
Firmware upgrade via back end Ethernet link
Readout Systems
A compact solution for large SiPM arrays

## Slide 68
DT5550W : ASIC Based Digital Acquisition system
MOTHERBOARD
PIGGY BACK BOARD
USB 3
LEMO I/O
FPGA with OPEN SOURCE FIRMWARE
Supported by:
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 69
DT5550W : ASIC Based Digital Acquisition system
DT5550W + PETIROC PIGGY BACK:
Up to 128 channels, multiple board can operate synchronized in order to extend channel count
Provide Bias to SiPM between 20 and 85V 10mA individually regulable
Amplification and programmable shaping of the SiPM output
Discriminator with independent threshold for each channel
Integrated TDC with 75 ps resolution
Charge measurements with 1024 channels energy spectrum generation
Configurable trigger logic:
  Or of all channels also between different ASICs
  Or of all channels of an ASIC
  Specific channel
  External trigger
  USER CONFIGURABLE TRIGGER/COINCIDENCE LOGIC USING SCI-COMPILER
USB 3 fast readout
Monitor of digital/analog probe signal with on-board ADC
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 70
Scalable systems
1-10 ch.
10-100 ch.
100-10000 ch.
Desktop / Handheld
Mini crates / enclosures
Crates / Racks
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 71
V1781: octal digital MCA (32k)
Based on V1724: 8 channel, 14 bit, 100 MS/s digitizer
VME version (2U wide) of the DT5781
BNC inputs (1 kΩ)
Coarse gain (analog): x1, x2, x4, x8 software selectable (0.125, 0.25, 0.5, 1 Vpp)
Dual range (jumper selectable): x1, x5
AC/DC coupling (jumper selectable) => supports Transistor Reset Preamplifiers
DPP-PHA firmware (Time stamped List Mode, Oscilloscope mode)
Improved PHA and trigger algorithms (inherited from Hexagon)
Coincidence/Anti-coincidence between channels. Ext Triggers (in and out, global and individual), veto, gate
Supported by MC2-Analyzer and CoMPASS
Best suited for Clover, Segmented Si/Ge detectors
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 72
V1741/DT5741: 64/32 ch, 16K peak sensing ADC
Based on V1740: 64 channel, 12 bit, 62.5 MS/s digitizer
Modified input stage: 4Vpp, 1 kΩ
Conversion Gain: 1k, 2k, 4k, 8k, 16k
Almost dead timeless (< 100 ns between gates)
Accepts negative and positive signals
Sliding scale (1/16 of the FSR) to reduce DNL (~1% @ 4K, t.b.d.)
Very good INL: <0.05% over 99% FSR
Multi Event Buffer (1K events per channel)
Zero Suppression with programmable threshold
Dedicated input for Event Rejection (PUR, Veto, etc…)
Three operating modes:
  External common gate
  External common trigger (gate generated internally with a programmable window)
  Independent self-triggering channels (future development on request)
Cable adapters for ERNI connector: 32 LEMO cables or two 34 wire ribbon cables (coming soon)
Works with N1068/N568
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 73
V2495/DT5495: user programmable logic unit
FPGA based Logic and Trigger Unit with customizable firmware
Up to 162 inputs, up to 130 outputs LVDS/ECL/PECL/NIM/TTL
Three expansion slots for digital I/Os and DACs
VME, USB2 and Ethernet(1) interfaces
32 programmable Gate & Delay lines
Sci-Compiler: Automatic VHDL generation starting from logic blocks and virtual instruments
Typical applications:
  Complex Trigger/Coincidence Logic (typically with Digitizers)
  Counters (Scalers) or Time stampers
  Low resolution TDCs (~ 0.5 ns)
  Replacement of NIM units (AND, OR, Timer, Fan In-Out, Translators)
  Programmable I/O register
  Pattern recorder/generator
  Threshold setting
(1) Desktop version only
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 74
Thank You!
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 75
BackUp
Digital Readout Electronics
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 76
HW+FW combinations
x724/x781 + DPP-PHA
  High energy resolution Gamma (and Alpha) Spectroscopy with HPGe, Clover and Silicon detectors
  Reads Charge Sensitive Preamps (RC or TRP) => Slow Signals (typ. 50 µs decay). No shaping amplifiers!
  Energy = Pulse Height (via Trapezoidal filter)
  No PHA histogram in HW: Time Stamped List Mode (10 ns)
  Coincidence, Anti-Coincidence, Veto, Gate, Neighbour Triggering options
  Possible to read scintillators (e.g. BGO) for Background or Anti-Compton shields
x725 + DPP-PHA
  Same as above, but lower cost per channel and slightly lower performance
  Better timing resolution (< 1 ns) thanks to zero crossing interpolation. Even better with x730+DPP-PHA
x730/x725 + DPP-PSD
  PMT/SiPM + Scintillation detectors (NaI, CsI, LaBr3, CeBr3, BaF2, ClyC, Liquid Cells, Plastic, etc…)
  Reads Anode signal => Fast signals (typ. 10/100 ns). No CSP/shaping needed
  Energy = Charge (gated integrator).
  PSD information (e.g. N/G discrimination) via dual integral (fast and slow components)
  Digital CFD+TDC: very good timing (100 ps order of magnitude)
  List Mode with T, E, PSD
  Coincidence, Anti-Coincidence, Veto, Gate (with some restrictions due to channel pairing)
x751 + DPP-PSD
  Same as above, but higher cost, lower Energy/PSD performance, better timing performance, better temperature stability
  No channel pairing
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 77
HW+FW combinations
x740 + DPP-QDC
  64 input, 4k MCA
  Low energy resolution Gamma Spectroscopy with scintillators (NaI, CsI, LaBr3 …)
  Can read direct anode from PMT or shaped signals from CSP (e.g. array of Position Sensitive Gas Tubes)
  Energy = Charge (gated integrator). List Mode with T + Q
  64 self-triggering independent channels
  8 channel grouping: limited capabilities to implement coincidences and complex trigger logic
x725/x730/x751 + ZLE
  Waveform recording with zero suppression/data reduction. Typically used for neutrino/dark matter experiments
  Triggered acquisition (typ. from beam or from dedicated trigger detector)
  Trigger-less acquisition: one channel fired above trigger threshold (high) => all channels acquire and apply ZLE with low threshold
  Simultaneous acquisition on all channels. Common time stamp: 1 trigger = 1 event
  No algorithms for energy, PSD…
  ZLE available for x724 and x720 too, but readout is slow (high dead time)
x725/x730/x724 + DAW
  Waveform recording with dynamically adapted acquisition window. Typically used for dark matter experiments
  Trigger-less acquisition: independent self-triggering channels
  Provides time stamp + waveform of variable length
  No algorithms for energy, PSD…
  Event building in SW
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 78
Readout interfaces
Optical Link (CONET 2)
  Requires a PCIe card in the host PC (A3818); can read up to 32 boards (up to 2048 channels)
  80 MB/s per board  aggregate bandwidth = 320 MB/s
  Low and predictable latency (typ. ~10 µs)
  Galvanic isolation
  Possible upgrade to ~300 MB/s (?) in the future
USB 2.0
  No external hardware required, plug and play
  30 MB/s per board
  Upgrade to USB 3.0 in the next generation digitizers
Ethernet
  Only supported by MCAs (DT5770, Hexagon, Gamma-Stream)
  Will be supported (up to 10 Gbps) in the next generation digitizers
VME
  up to 200 MB/s in 2eSST mode (Bandwidth shared between boards in the crate)
  SBC required for 2eSST; PCI bridges A3818/V2718 support BLT/MBLT only (up to 80 MB/s)
  NOTE: the usage of the VME bus for communication is discouraged. Front panel readout is backplane independent. VME used for power supply, ventilation and mechanics
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 79
Multi-Board Readout example (Xmass)
16 digitizers in one VME crate read out by 1 computer @ 350 MB/s
One 4 link A3818 PCIe card. Each link reads 4 digitizers in daisy chain
~22 MB/s per digitizer (can be 4 times higher in a P-to-P topology)
VME crate just for power and mechanics (no backplane communication)
350 MB/s
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 80
General Architecture
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 81
DPP PHA: Block Diagram
Fast
Timing
Filter
ENERGY
Energy
Filter
ZC
BLR
ICRFF
Peak
(Flat Top)
PUR
TDC
sync
TIME STAMP
OCR
FADC
DIGITAL
ANALOG
Trapezoidal
Shaper
Fine Gain,
Shaping Time,
PZ cancel
Coarse Gain
xG
Preamp
(embedded)
LLD thr
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 82
DPP PHA: signals
INPUT (from PA)
TIMING FILTER
(FAST DISCRIM)
ICRFF
ENERGY FILTER
(TRAPEZOIDAL)
OCR
T1
T2
T3
T4
T5
E1
E2
E3
T6
P1
P2
P3
P4
P5
P6
P7
E6+E7
Pile Up
Unresolved
Double Pulse
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 83
DPP-PHA: Pile-up Rejection and Dead Time
The waveform digitizer operates continuously => No dead time in A/D conversion.
Dead time due to algorithms (pulse processing), not to electronics
Energy Filter:
T5-T4 < Trapez(Rise+Flat) => pile-up => Get time stamps (ICRFF), no energies (OCR) DeadTimeTRAPEZ (%) = 100 * (ICRFF - OCR) / ICRFF
T3-T2 < Trapez(Rise+Flat+Fall) => no pile-up (get T and E), but no fresh baseline for E3 => worse resolution. It is possible to extend the PUR window and allow BLR to recover for every pulse ("Peak Hold-off")
Fast Timing Filter:
T7-T6 < Double Pulse Resolution (Typ. 300-500 ns) => summed pulses => get single T, E (=E6+E7) Sum peaks in the energy spectrum. Dead time (paralyzable) corrected on statistical base: ICRFF = ICR * exp (- ICR * TDPR) where TDPR is the double pulse resolution (i.e. resolving time)
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 84
DPP PSD/QDC: Block Diagram
Timing
Filter
ENERGY
Delay
Discr
ICR
TDC
sync
TIME STAMP
DIGITAL
ANALOG
BLR
Gate
Generator
QDCS
Ratio
FADC
PSD
QDCL
PUR
OCR
LONG
SHORT
CFD/LED
Coarse Gain (= Qsens)
ANODE SIGNAL
PreTrigger
Threshold
Coinc/Veto
Width
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 85
DPP PSD/QDC: signals
Input from PMT
CFD
Long Gate
ZC = TIME STAMP
Short Gate
Trigger
QS = FAST
QL – QS = TAIL
PSD =
TAIL
TOTAL
QL=TOTAL=ENERGY
THRESHOLD
Baseline
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 86
Digital CFD + TDC
INPUT
CFD
A
B
CLK
TRIGGER
ZC FINE TSTAMP
COARSE TSTAMP
digital CFD: same principle as analog
CFDN+1 = f * SN - SN-D f=Fraction, D=delay
Linear interpolation A-B:
COARSE TSTAMP = TCLK * Clock Counter
FINE TSTAMP = TCLK * B/(A-B)
good fit if Leading-Edge > 3-5 TSAMPLE
Faster signals produce artifacts and degradation of the timing resolution
ZC calibration algorithm corrects interpolation errors for signals as fast as ½ TSAMPLE
~10 ps RMS for 1 ns rising edge @ 500 MS/s
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 87
Digital CFD: results
Test | Rise Time | Amplitude | ZC corr | Start-Stop Resolution | 
 |  |  |  | RMS | FWHM
Pulse Generator | 1 ns | 450 mV |  | 9.5 ps | 22 ps
Pulse Generator | 5 ns | 450 mV |  | 10.1 ps | 24 ps
Pulse Generator | 20 ns | 450 mV |  | 1.9 ps | 4.5 ps
BaF2 to BaF2 | 1.3 ns | 130 mV |  | 120 ps | 280 ps
BaF2 to BaF2 | 1.3 ns | 130 mV |  | 538 ps | 1.3 ns
BaF2 to LaBr3 | 1.3/15 ns | 130/200 mV |  | 186 ps | 437 ps
NaI to NaI | 20 ns | 100 mV |  | 1.02 ns | 2.40 ns
Single Detector Resolution |  |  |  | 
Detector Type | Size | PMT | TRES (FWHM) | Notes
BaF2 | 1" | H3378-51 | 200 ps | 
LaBr3 | 2" | R6231 | ~ 400 ps | extrapolated from BaF2 to LaBr3 Timing
NaI (Tl) | 2" | ETL 9266 | 1.7 ns | 
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 88
Compass: root based DAQ
Multi-board, multi-channel, multi-parametric: Energy, Time, PSD
Root data format: T-tree, 1-D and 2-D histograms
Coincidences (HW or SW), veto/gate, cuts and event selection
Acquisition mode: live (from boards) or off-line (from data files)
Supported Boards & FW:
x724/x781 PHA
x725/x730 PHA
x725/x730 PSD
x751 PSD
x720 PSD/CI
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 89
Compass: block diagram
HW
Readout
Server
Configuration GUI
HW
HW
Spectra
T-tree
Plots
&
Stats
Config
Output
Socket
Sorted
List
E,T,PSD
Spectra
Config File
ROOT
Raw Data
Sort
Select
Scan
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 90
ZLE/DAW firmware for x725/x730
ZLE
Raw Waveform acquisition with zero suppression: extraction of chunks from a fixed size window
Common trigger (simultaneous acquisition on all channels)
Channel self-triggers (digital discriminators) can generate the common trigger (masked OR)
Baseline subtraction
Max 16/32 µs acquisition window for x730/x725 respectively
Separate thresholds for trigger and ZS: typically high threshold for triggering (well above noise, to prevent false triggering), lower threshold for zero suppression (to acquire small pulses at the noise level)
Event Building in HW (1 trigger => N channels)
DAW
Raw Waveform acquisition with independent self-triggering channels
Acquisition window dynamically adapted to the pulse width
Baseline subtraction
“Unlimited” acquisition window
Event Building in SW by time stamp sorting
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 91
STD firmware
Incomplete
Pulse
Empty Channel
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 92
ZLE firmware
Incomplete
Pulse
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 93
DAW firmware
Missing
Pulse
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 94
DPP firmware
Missing
Pulse
Incomplete Pulse, Wrong Energy
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 95
Hexagon: Single/Dual 32k Digital MCA
Fully integrated, digital MCA operating in PHA mode (up to 32k), Time stamped List mode, MCS(*), SCA(*), Multi-PHA(*).
Suitable for HPGe, Si, NaI, CsI, LaBr3, CdTe, CZT and other detectors. Accepts RC and TRP preamps and PMT anode signals.
Embedded Linux (ARM) for unattended acquisition, data logging (SDD), user programmable routines (SDK provided).
Dual range HV: 5kV/20µA (HPGe mode) or 2kV/1mA (PMT mode), positive/negative.
10/100T Ethernet and USB 2.0 interfaces. OLED Display. Configurable digital I/Os and Sync bus.
Coincidence and Anti-Coincidence mode (e.g. Anti-Compton or Background Active Shields)
(*) work in progress
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 96
Acquisition Modes
PHA: 1k to 32k, 32 bit depth, Start/Stop from SW, external TTL input or SyncBus (multiple MCAs)
Time stamped List Mode (Resolution = 10 ns)
SCA(*): programmable LLD and ULD; can drive TTL outputs, internal readable counters, MCS and Signal Inspector
MCS(*): counts on Fast Discriminator, SCA or external inputs; programmable Dwell time or external Channel Advance command; Sweep Start command from SW or external input.
Multi-PHA(*): series of consecutive PHA spectra; SW or external TTL input Spectrum Advance command. No dead-time while switching to a new spectrum
Coincidence/Anti-Coincidence: between 2 channels and/or external NIM/TTL Inputs. Applies to PHA, List Mode, SCA and MCS. Programmable coincidence window. Suitable for Anti-Compton or Background Active Shields with scintillators (e.g. CH0 reads HPGe, CH1 reads shield)
Signal Inspection: mixed signal oscilloscope for detector signals, internal filters, control signals and flags; SCA or event driven waveform capture (e.g. see the pulses that generate events in a ROI)
Local storage of spectra and lists on SDD for unattended mode (no need of external PC control)
(*) work in progress
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 97
ADC
Input Connector: BNC (~600 ohm)
Coupling: DC or AC with three differentiation time constants (5, 12, 30 µs)
SW controlled analogic Pole-Zero compensation for AC coupling. Manual or Auto(*) set.
Positive or negative inputs
Supports RC and TRP Preamps as well as direct PMT Anode signals
Throughput: tested up to 200 Kcps (max. rate T.B.D.)
Conversion Gain: 32K, 16K, 8K, 4K, 2K, 1K computer selectable
Coarse Gain: 1, 2, 4, 8, 16, 32, 64, 128, 256 (Coarse Gain=1 corresponds to 1 Vpp input range)
Input Attenuator: 0.25 software selectable
Fine Gain (digital): 1 to 2.2, increments < 0.0001
DC offset programmable in the full range
INL 0.05% for Coarse Gain < 8; 0.1% for higher gains
DNL: < ±1% over 99% of the FSR
FWHM Resolution: 0.61 keV @ 122 keV, 1.63 keV @ 1332 keV (tested with HPGe Mod. Canberra Cryo-Pulse 5 Plus Electrically Refrigerated Cryostat, equipped with iPa Preamp)
Dynamics: down to 4 keV with 3 MeV FSR (noise peak at same height of compton)
(*) work in progress
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 98
Digital Processing
Energy Trapezoidal Filter: Rise time 0.02 to 40 µs, Flat Top 0.02 to 20 µs
Pole-Zero compensation (exponential decay time): from 0.1 to 650 µs. Manual or Auto(*) set.
Fast Discriminator: double Triangular Filter; shaping time 0.01 to 2.4 µs. Manual or Auto (*) Threshold
Pulse Pair Resolution: typ. 0.5 µs (with triangular shaping time = 1 µs)
Trigger hold-off (imposed dead-time) to prevent after pulses or overshoot retriggering: 0 to 40 µs
Programmable Pile-up Guard Duration: 0 to 80 µs beyond the end of the flat top
Baseline Restorer: fast, medium, slow
Low Frequency Rejector for electrical cooling (microphonic noise suppression)
Dead-time correction: error < 5% on the net area of a static reference source offended by a variable rate source ranging from 1 to 100 Kcps (at fixed live time Preset)
(*) work in progress
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 99
Power Supply
High Voltage:
2 HV channels (P-P, N-N or P-N, ordering option) on SHV connectors
Dual range (software selectable): HPGe/Si (0.02 to 5 kV, 30 µA) or PMT (0.02 to 2 kV, 1 mA)
Ripple < 5 mVpp
2 inhibit inputs on BNC (SW selectable active high or low, TTL threshold, accepts from -12V to 12V)
The Inhibit is replicated on DB9 connectors
Programmable Ramps: 1 to 500 V/s
Low Voltage:
Two independent DB9 connectors
Preamp power supply: ±12V, 100 mA; ± 24V, 50 mA
Temperature or Nitrogen level sensor readout
Additional HV Inhibit (ORed with BNC)
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 100
Inputs/Outputs
Two BNC inputs for ADC Gate or Veto (e.g. TRP inhibit, Coincidences, etc…). Accepts TTL and NIM. Gate and Inhibit duration can be as long as the input signal or equal to a programmable time (0.01 µs to 160 ms)
Two BNC inputs for HV inhibit (TTL threshold, accepts from -12V to 12V, pulled-up, active high/low by SW)
Sync Bus In/Out (two SATA connectors) for clock and time stamp reset.
One BNC analog output for real time signal inspection (reproduces inputs or internal digital filters). 4 Vpp.
24 Programmable TTL I/Os on DB25 connector (BNC adapter available on request):
  Acquisition Start/Stop Input
  MCS Inputs for Start, Advance, Count (*)
  SCA Output (*)
  ICR Output
  Run Output
  Sample Changer Output (*)
  Sample Ready Input (*)
  User programmable I/Os (*)
(*) work in progress
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 101
Displays
OLED Graphic Display
ICR, OCR
Real, Live, Dead Time
HV settings and monitor (Voltage and Current)
Two push buttons to toggle between channels 0/1 and to cycle screens
LEDs
Front Panel: PowerON on push button, Status (bi-color: ready/run/busy), Communication, HV failure (inhibit or overcurrent), incoming pulses on ADC inputs, activity on Gate/Veto inputs
Rear Panel: HV polarity, HV ON, HV OverCurrent, HV Inhibit, SyncBus connected, Ethernet activity
Interfaces
10/100T Ethernet
USB 2.0 (micro USB)
Drivers, Libraries, Software and Manual preloaded on SDD (autoplay)
Web Interface planned for 2019
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 102
Hexagon Performances: Resolution (tested with HPGe Mod. Canberra 7229P, Preamp 2001C)
Chart: Trapezoidal Rise Time (us)
| 1 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16
Co60 @ 1332 KeV | 1.985 | 1.732 | 1.728 | 1.673 | 1.685 | 1.636 | 1.708 | 1.645 | 1.759
Co60 @ 1173 KeV | 1.973 | 1.654 | 1.634 | 1.581 | 1.608 | 1.589 | 1.578 | 1.623 | 1.696
Co57 @ 122 KeV | 1.346 | 1.069 | 0.891 | 0.83 | 0.812 | 0.817 | 0.827 | 0.865 | 0.86
Cs137 @ 662 KeV | 1.613 | 1.456 | 1.303 | 1.261 | 1.261 | 1.274 | 1.282 | 1.28 | 1.321
Chart: Energy (keV)
| 122 | 662 | 1173 | 1332
1 us | 1.346 | 1.613 | 1.973 | 1.985
2 us | 1.069 | 1.456 | 1.654 | 1.732
4 us | 0.891 | 1.303 | 1.634 | 1.728
8 us | 0.812 | 1.261 | 1.608 | 1.685
12 us | 0.827 | 1.282 | 1.578 | 1.708
Chart: Coarse Gain
| 0.25 | 0.5 | 1 | 2 | 4 | 8 | 16
Co57 @ 122 KeV | 0.985 | 0.861 | 0.812 | 0.807 | 0.8 | 0.796 | 0.798
Chart: ICR (kHz)
| 2 | 10 | 20 | 50
1332 keV (Trise 1us) | 2.17 | 2.197 | 2.182 | 2.249
1332 keV (Trise 4us) | 1.8 | 1.842 | 1.859 | 2.031
1332 keV (Trise 7us) | 1.751 | 1.811 | 1.878 | 2.235
1332 keV (Trise 10us) | 1.763 | 1.875 | 1.99 | 2.758
Trise = 10 us
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 103
Hexagon Performances: Peak shift and dead time
(tested with HPGe Mod. Canberra 7229P, Preamp 2001C)
Chart: Peak Shift vs ICR
| 2 | 10 | 20 | 50
1332 keV (Trise 1us) | 0 | 0.011763 | 0.023527 | 0.094107
1332 keV (Trise 4us) | 0 | 0.011862 | 0.023725 | 0.071174
1332 keV (Trise 7us) | 0 | 0.023761 | 0.035642 | 0.059404
1332 keV (Trise 10us) | 0 | 0 | 0.023781 | 0.035672
Chart: Dead Time vs ICR
| 2 | 10 | 20 | 50
Trise 1us | 4.26 | 11 | 18.07 | 41.44
Trise 4us | 6.45 | 16.46 | 23.43 | 56.34
Trise 7us | 7.55 | 21.01 | 33.69 | 67.28
Trise 10us | 8.54 | 25.56 | 40.19 | 75.44
Chart: Net/Live vs ICR
| 2 | 10 | 20 | 50
1332 keV (Trise 1us) | 1 | 0.98454 | 0.96404 | 0.95942
1332 keV (Trise 4us) | 1 | 0.99064 | 0.99071 | 0.96667
1332 keV (Trise 7us) | 1 | 0.98267 | 0.97759 | 0.95272
1332 keV (Trise 10us) | 1 | 0.97169 | 0.94494 | 0.95382
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 104
Software for Hexagon (and other MCAs)
MC2 Analyzer 2.0:
Multi Board Configuration and Acquisition Software
PHA and List Modes
Presets: real time, live time, total counts
Coincidences/Anti-coincidences
ROI, energy calibration, FWHM, statistics
Mixed signal Oscilloscope for Signal Inspection
SDK:
Drivers and Libraries for custom SW development
User access to embedded Linux (ARM)
Coming soon:
Full featured configuration, acquisition and analysis software
PHA, MCS and List modes
Peak Search and ROIs
Energy, Efficiency and FWHM calibration
Isotope libraries and identification
Quantitative analysis and reports
Jobs and Presets management
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 105
BackUp
SiPM Readout Electronics
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 106
i-Spector: PMT replacement with integrated digital pulse processing
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 107
i-Spector: PMT replacement with integrated digital pulse processing
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 108
i-Spector: PMT replacement with integrated digital pulse processing
NO SOFTWARE INSTALLATION REQUIRED
INTEGRATED WEB-APP
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 109
i-Spector: PMT replacement with integrated digital pulse processing
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 110
i-Spector: PMT replacement with integrated digital pulse processing
OEM
BOXED COUPLED WITH SCINTILLATOR
Accessory
CsI(Ti)
BGO
LaBr
Available versions:
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 111
i-Spector: PMT replacement with integrated digital pulse processing
Scintillator
SiPM
Q-PRE
HV
Temperature feedback
FAST ANALOG
OUT (LEMO)
ADC
MCA
uCU + WEBSERVER
LORA
LAN
DUAL LEMO
PROGRAMMABLE IN/OUT
TMU
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 112
i-Spector: PMT replacement with integrated digital pulse processing
Digital MCA + PSD + Fast Digitizer
Q4-2019
(estimated)
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 113
i-Spector: PMT replacement with integrated digital pulse processing
Analog Output Only:
Woks exactly as a PMT but with integrated bias and charge amplifier
Integrated charge amplifier with fast shaping
Output capable to drive 50R load
Integrated MCU to remote control and program Bias
Ethernet connectivity
SiPM HV
Automatic temperature compensation with HV feedback
Operate from 6 to 18V
Scintillator
SiPM
Q-PRE
HV
Temperature feedback
FAST ANALOG
OUT (LEMO)
uCU + WEBSERVER
LAN
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 114
i-Spector: PMT replacement with integrated digital pulse processing
TMU (Time Measurement Unit):
Replace PMT, Pre, Discriminator, and all time-based unit like coincidence/veto/trigger logic, scaler, TDC, timestamp, time of flight spectrum
Scintillator
SiPM
Q-PRE
Timing or LORA
HV
Temperature feedback
FAST ANALOG
OUT (LEMO)
uCU + WEBSERVER
LAN
DUAL LEMO
PROGRAMMABLE IN/OUT
i-Spector PLUS
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 115
i-Spector: PMT replacement with integrated digital pulse processing
LEMO CABLE
DT1: 122123
DT2: 1112
COINC: 123
COINCIDENCE COUNTER
TRIGGER OUT
LEMO CABLES
MULTI-DEVICE TRIGGER SYSTEM
SINGLE WINDOW ANALYSER
122211

## Slide 116
i-Spector: PMT replacement with integrated digital pulse processing
LEMO CABLE
TOF SPECTRUM
PROTON
NEUTRON
RATE METER
122211
EVENT TIMESTAMP
Pulsed Source
Event 1: 150 ps
Event 2: 4554 ps
….
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 117
i-Spector: PMT replacement with integrated digital pulse processing
MCA (MultiChannel Analyzer) + waveform digitizer
Replace PMT, Pre, Discriminator, and digitizer with PHA. Integrate digital charge integrator and produce a spectrum as output.
4096 channels spectrum
80 Msps, 12bit low power ADC
Oscilloscope mode to monitor detector signal output
Can operate in spectrum and list mode (in list mode max rate:100kcps)
Web-based software, with spectrum analysis tools: ROI, fitting, energy calibration
Will be compatible with MC2
Scintillator
SiPM
Q-PRE
HV
Temperature feedback
FAST ANALOG
OUT (LEMO)
ADC
MCA
uCU + WEBSERVER
LAN
ADC
TRIGGER
BASELINE
CHARGE
INT
SPECTRUM
uC
SHAPER
PRE
SiPM
ANALOG OUTPUT
ON LEMO
LIST MODE
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 118
i-Spector: PMT replacement with integrated digital pulse processing

## Slide 119
i-Spector: PMT replacement with integrated digital pulse processing
MCA + Wireless module:
Integrate the MCA and a LORA (LORAWAN compatible) mode
Long range communication:
  10 Km sight view (30 km with directional antenna)
  Up to 1 Km internal building
Can be linked to commercial LORAWAN gateway (inexpensive infrastructure)
MCA with 4096 channels
Basic online isotope identification (counts in configurable windows)
Possibility to set alarms
Can be powered by a small solar panel
We offer customization service to end-user customer in order to develop the data collection system
Scintillator
SiPM
Q-PRE
HV
Temperature feedback
FAST ANALOG
OUT (LEMO)
ADC
MCA
uCU + WEBSERVER
LoRa
LAN
i-Spector Digital LoRa
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 120
i-Spector: PMT replacement with integrated digital pulse processing
Target customer:
This product cover the largest part of the market of PMT (I can’t say the percentage) so:
    ANYONE IS USING OR IS GOING TO USE A PMT FOR SOMETHING
Laboratory experimenters (replace detector, HV, MCA, TDC)
  Spectroscopy based on scintillator
  Timing application
  ….
Large experiment (replace detector, modular logic, TDC):
  Veto / Coincidence
  Trigger
Homeland Security:
  Disseminated monitor net
  Portals
LOOK AHEAD PHYSIC APPLICATION: molecular fluorescence, lidar, astronomy, …
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 121
DT5550W : ASIC Based Digital Acquisition system
MATRIX 1
MATRIX 2
A7585
HV
PETIROC
PETIROC
PETIROC
PETIROC
FPGA
USB 3
DIGITAL READOUT
CH [0..63]
CH [64..127]
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 122
DT5550W : ASIC Based Digital Acquisition system
MATRIX 1
MATRIX 2
A7585
HV
CITIROC
CITIROC
CITIROC
CITIROC
FPGA
USB 3
MULTIPLEXED READOUT
ADC
8ch
80Msps
14 bit
CH [0..63]
CH [64..127]
Simultaneous readout of 128 channels in low and high gain mode
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 123
DT5550W : ASIC Based Digital Acquisition system
HAMAMATSU
S13361-3050AE-08
IDC CONNECTOR (STRIP 2.54mm PITCH) ADAPTER
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 124
DT5550W : ASIC Based Digital Acquisition system
Target customer:
Easy solution to capture a large amount of channels:
  Plug and play solution with full featured software
  Software process online data reconstructing clusters between ASIC
  Direct compatible with a ready-to-use Hama matrix 8x8 Detector (if you order DT+A+MATRIX you receive a kit to immediately start to make a measure)
User looking a ready to use solution to readout multiple SiPM matrix/array
  User who have its own pixelated detector and is looking for a readout (will use cable adapter)
  User who have an idea of experiment and is looking for a full readout system (will use the Hama compatible detector)
User wants to test Weeroc ASIC with in a real acquisition system
Large experiment: multiple board can operate together and synchronously
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 125
DT5702 : 32 channels SiPM readout system based on CITIROC
TRADITIONAL FIRMWARE
Providing basic coincidence of signals from each pair of adjacent even-odd channels
Allows to trigger only on events that happen in coincidence with event in a group of other A1702 (event validation)
Two trigger logic:
  All channel fire a trigger
  Plane coincidence
32 CH
OR
0
1
14
15
…
16
17
30
31
…
PLANE
COINCIDENCE
Flag the first triggering channel
NEW FIRMWARE
1 ns timestamp resolution
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 126
DT5550AFES + DT5550 : SiPM detectors Digitization System
Target customer:
Researcher involved in SiPM characterization:
  Everyone wants a 64 channel oscilloscope to see the single waveform simultaneously captured on all channels.
Calorimetry experiment (has been designed for a SiPM based calorimeter):
  Where a large dynamic range is required (no ASICs at the moment have comparable performance)
High rate application (up to 1Mcps with the possibility to operate faster reducing energy resolution)
High resolution spectroscopy: this is the solution with better performance on the market I have notice for SiPM
Application where the number of channels is not so big to require absolutely an ASIC and more versatility is a requirement; this product is supported by SCICOMPILER and full processing chain can be customized
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 127
BackUp
Detector Emulators and Signal Generators
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 128
Family Comparison
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited
SP5601/SP5605: fast LED driver with tunable intensity and repetition rate.
• Pulse width: 8 ns / 4ns
• LED color: Violet (400 nm), 1500 mcd / color: UV (245 nm), 0-27000 photons
• Pulse generator: internal/external
• Output Frequency: From 500Hz to 5 MHz /From 100 Hz to 1500 Hz
DT4700 Clock Generator
• 50 MHz and 62.5 MHz clock frequencies available and switch selectable
• Possibility of propagating a clock from another external source
• 10 differential outputs
• USB powered
DT5810:
1 ns rise time
Analog input
More bandwidth in noise emulation
Longer waveform in AWG mode
DT5800:
12 ps resolution correlation
8 ns rise time
Good compromise Performance/Price
DT4800:
Very cost effective
Good for educational purposes
Compact form factor

## Slide 129
BackUp
Other Projects
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited

## Slide 130
A2795: 64 ch, Argon TPC Readout System
Complete readout system for Liquid Argon TPC
Preamps: plug-in hybrid circuit
ADC: 12 bit, 2.5 MS/s
Acquisition Mode: simultaneous waveform acquisition with External Trigger
Memory: max. 16 x 4k samples (~1.6 ms each)
TT-Link: 1-wire link for trigger and timing distribution
CONET2 interface: 80 MB/s daisy chainable Optical Link (controlled by A3818 PCIe cards)
Custom crate connected to detector flange
Reproduction, transfer, distribution of part or all of the contents in this document in any form without prior written permission of CAEN S.p.A. is prohibited