## Slide 1: Information about the proposal for the opening of a new theme "Development of the Conceptual Design of a New Advanced Neutron Source at JINR"
V. Shvetsov
50th meeting of the PAC for Nuclear Physics
June 24-25, 2019, JINR, Dubna, Russia

## Slide 2: Content
Historical introduction;
Research in the field of condensed matter physics in Dubna;
The IBR-2 pulsed reactor, status and prospects;
World trends in the development of the neutron sources;
Current status of the development of conceptual design of a new neutron source at JINR;
Resource requirements;
Conclusion;

## Slide 3: Historical introduction

## Slide 4: Historical introduction

## Slide 5: IBR, IBR-30, IBR-2
IBR reactor – one of the worlds first dedicated for experiments on extracted beams;
Condensed matter physics – one of the three scientific “pillars” of the Joint Institute;
First experiments on CMP at the Laboratory of Neutron Physics of JINR started in early 60-th by initiative of F.Shapiro, J.Janik and B.Buras;
Effective development of the neutron instrumentation in parallel with construction of the new neutron sources;

## Slide 6: Research in the field of condensed matter physics in Dubna

## Slide 7: Research directions and instrumentation development
High temperature superconductors;
Soft matter, gels, polymers;
Chemistry, real time experiments;
Biology, ribosome and proteins structure;
Materials science, engineering analysis, mechanical stresses;
Neutron diffraction at extreme conditions;
Small angle scattering;
Inelastic scattering spectrometers;
TOF Fourier diffractometry;
Reflectometry of polarized neutrons;
Pulsed action on the sample, synchronized with the neutron pulse;

## Slide 8: 2018 results
203 papers in referred magazines;
208 reports at the international conferences;
3 patents;
40 students participated in the research;

## Slide 9
FLNP JINR:
2 plenary lectures
8 invited talks
20 oral presentations
31 poster

## Slide 10: The IBR-2 pulsed reactor, status and prospects

## Slide 11
Notes: IBR-2 is a pulsed fast reactor of periodic operation. Its main difference from other reactors consists in mechanical reactivity modulation by a movable reflector. The movable reflector is a complex mechanical system providing reliable operation of two parts, which determine the reactivity modulation: the main movable reflector and the auxiliary movable reflector. The rotors of the main and auxiliary movable reflectors rotate in opposite directions with different velocities. The IBR-2 reactor with its unique technical approach produces one of the most intense neutron fluxes at the moderator surface among the world's reactors: ~10^16 n/cm2/s, with a peak power of 1850 MW. Nevertheless, the reactor is "ecologically friendly": it consumes very little electrical energy as compared to other research reactors, uses a very little amount of fuel (less than 20 l) which is changed once in 15-20 years. The reactor operates continuously for a 12 day cycle followed by a week shutdown to prepare for the next experiments. In addition, there is a longer shutdown to carry out necessary maintenance work during the summer time. Normally there are about 9 cycles a year.

## Slide 12
Notes: The main objectives of research at the IBR-2 involved the application of neutron scattering techniques and complementary methods to investigate the structure, dynamics and microscopic properties of nanosystems and novel materials, which are of great importance for the development of nanotechnologies in the fields of electronics, pharmacology, medicine, chemistry, modern condensed matter physics and interdisciplinary sciences. A list of the main scientific topics includes:
 Investigation of the structure and properties of novel functional materials;
 Investigation of the structure and properties of materials under extreme conditions (high pressure – up to 500 kbar, cryogenic temperatures, high magnetic fields);
 Investigation of fundamental regularities of real-time processes in condensed matter;
 Investigation of atomic dynamics of materials for nuclear power engineering;
 Computer simulation of physical and chemical properties of novel crystalline and
nanostructured materials;
 Investigation of magnetic properties of layered nanostructures;
 Investigation of structural characteristics of carbon- and silicon-containing nanomaterials;
 Investigation of molecular dynamics of nanomaterials;
 Investigation of magnetic colloidal systems in bulk and at interfaces;
 Structural analysis of polymer nanodispersed materials;
 Investigation of supramolecular structure and functional characteristics of biological materials;
 Investigation of structure and properties of lipid membranes and lipid complexes;
 Investigation of texture and physical properties of Earth’s rocks, minerals and engineering
materials;
 Non-destructive control of internal stresses in industrial products and engineering materials;
 Introscopy of internal structure and processes in industrial products, rocks and natural
heritage objects

## Slide 13: User policy at IBR-2 facilities
18 facilities around the reactor;
15 instruments for condensed matter studies are now presented for users;
Simple, convenient web-application;
Two calls/year;
No charge for beam time except of commercial use;
Since 2020 Radioanalytical Laboratory with NAA will be introduced as user facility;

## Slide 14: Comparison of the effectiveness of the IBR-2 instruments with the instruments at European sources
We have about 160 neutron instruments at 13 European neutron sources, generating almost 30000 instrument days, resulting 1900 scientific papers each year;
16 instrument days/paper at European instrument
At IBR-2 we have 15 instruments, operating about 2500 hours per year, that generates about 1563 instrument days, resulting about 90 scientific papers each year;
17 instrument days/paper at IBR-2 instrument

## Slide 15: World trends in the development of the neutron sources

## Slide 16: Why do we need new source?
In order to preserve condensed matter physics as one of the three scientific pillars of JINR, we need a new world-class source that will replace the IBR-2 reactor after the end of its service life;
The period of ageing of the modern scientific facilities is increasing;
All developed countries are planning construction of the new neutron sources with extracted beams for neutron scattering and nuclear physics;
Thermal neutron flux density on the moderator surface (2 equivalent): average not less than 1014 n/cm2/s, peak not less than 1017 n/cm2/s

## Slide 17: What we can do with slow neutrons except condensed matter investigations
Baryogenesis, CP violation, and the neutron electric dipole moment;
  The role of the neutron in element formation;
    Primordial nucleosynthesis;
    Stellar nucleosynthesis;
Baryon-number violation, mirror universes, and neutron oscillations;
Extra dimensions, new forces, and the free fall of the neutron;
  Gravitational quantum levels;
  Gravitational versus inertial mass;
The electroweak standard model and the -decay of free neutrons;

## Slide 18
2015

## Slide 19
2032 ?

## Slide 21
1. Investigations performed at neutron sources are essential components of R&D in numerous areas of science and engineering.
2. Neutron scattering is often an essential part of a broader experimental study that uses a complementary suite of tools (e.g., light sources, high-performance computers). Thus, neutron sources play a key role in overall U.S. innovation capacity.
3. The United States has lost important capability in neutron R&D in the last two decades and is no longer the world leader. The United States cannot afford to lose its remaining capacity and capability without significant detriment to the quality and quantity of science, engineering, and even medical and manufacturing processes that rely on neutron sources.
4. Reactor fuels containing HEU represent a risk for proliferation, which should be considered when planning for the future infrastructure for neutron R&D.
5. Current HEU-fueled research reactors provide unique R&D capabilities relative to other neutron sources available today. Eliminating them without developing and deploying alternative methods of producing neutrons with the same properties
(e.g., from high-density LEU-fueled reactors and/or a new generation of spallation sources) would compromise U.S. innovation capacity.
6. World-class neutron science and engineering require the comprehensive benefits of spallation facilities, research reactors, and high-performance instrumentation. While there is some overlap in the capabilities provided by spallation and reactor sources, each provides certain capabilities that cannot now be duplicated by the other type of source.

## Slide 22: Current status of the development of conceptual design of a new neutron source at JINR

## Slide 23
N. Kučerka & E.V. Lychagin: Development of the scientific case for a new source of neutrons at JINR
E. Shabalin & Yu.N. Pepelyshev: Concepts of JINR’s high-flux pulsed neutron source
V.N. Shvetsov & V.L. Aksenov: Milestones and time schedule proposal to the strategy plan of JINR
PuO2 based superbooster
Progress outline:
A superbooster (multiplying target of proton linear accelerator with periodic reactivity modulation) is being considered for the new neutron source
Feasibility study of 2 concepts (neptunium and plutonium based) has been started
Time schedule road map has been developed that establishes 6 major stages and proposes the finalization in 2035 – replacing the present source IBR-2M smoothly
Dubna Neutron Source of the Fourth Generation two options
Notes: In accordance to the 7-year plan and long-term strategic planning of JINR, the Frank Laboratory of Neutron Physics has initiated project for the realization of new JINR source of neutrons. In addition to developing the case for scientific justification, discussions are carried out regarding the type of this new source. A superbooster (multiplying target of proton linear accelerator with periodic reactivity modulation) has been concluded to be able to provide record parameters desired by physicists. Recently, the feasibility study of 2 most appealing concepts has been ordered at NIKIET, and time schedule road map has been developed that will allow a timely and smooth replacement of the present source IBR-2M.

## Slide 24: At present we have contract with NIKIET on feasibility study of the:
Pulsed reactor with mechanical modulation of reactivity, based on Np fuel;
ADS with mechanical modulation of reactivity (super booster), based on PuO2 fuel;

## Slide 25: PROJECT ROADMAP (preliminary)
Stage | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37
Concept development |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Conceptual design |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Investment justification |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
R&D |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Technical design |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Construction |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Commissioning |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 26: Basic parameters of the reactor
Parameter | Value
1 Average thermal power, MW | 15
2 Operational mode | pulsed
3 Repetition rate, Hz | 10
4 Fuel | NpN
5 Coolant | Na
6 Inlet temperature of the coolant, 0С | 290
7 Outlet temperature of the coolant, 0С | 391
8 Coolant flow through ½ of the core, kg/s | 58
9 Pressure drop across the core, Pa | 0,33·105
10 Fast neutrons flux density on the reactor vessel, 1014 n/cm2·s1 | 5,7
11 Fluence on the reactor vessel for 20 000 hours, n/cm2 | 4,1·1022

## Slide 27: General view of the reactor in the bulk concrete
IC
Shutter
Stationary reflector
Reactivity modulator
Ø 6m
Ø 2m

## Slide 28: Control
CR-3 (TiH2)
AR-2 (Ni)
EP-2 (Ni)
CR-4 (TiH2)
CR-2 (Ni)
CR-1 (Ni)
EP-1 (Ni)
AR-1 (Ni)

## Slide 29
Beams – Moderators
Moderator | Amount of beams (first stage) | Temperature, K | Size, mm | Possible material
bi-spectral | 2 | Cold 80-90 K + warm 300 K (one above the other) | 100x100 + 100x100 | (Liquid methane/ethane/ pelletized mesitylene)+water
cold | 4 | 80-90K | 200 x 200 | Liquid methane/ethane/ pelletized mesitylene
very cold | 3 | <30K | 200 x 200 | Pelletized solid methane/parahydrogen/pelletized mesitylene
very cold | 6 | <30K | 100 x 100 | Pelletized solid methane/parahydrogen/pelletized mesitylene

## Slide 30
32 beamports with
10° separation:
For instruments:
4 – bi spectral
8 – large cold
8 – large very cold
8 – small cold
4- small tangential cold
2- small/tangential/cold (80K)
2- small/ tangential/ very cold (<30K)
4 – bi spectral
(300+80K)
4– small /cold
(80K)
4 – small/ cold (80K)
8 – large/ very cold (<30K)
8 – large cold (80K)
Be reflector
Water pre-moderators
Core

## Slide 31
The basic set of 15 neutron TOF instruments for the first stage +
~ 10 instruments for the second stage
Moderator
Instrument Main issue T, K Size, cm
1. Material science*) Internal stresses 300 / 80 K 10x10
2. High-resolution*) Crystal structure 300 / 80 K 10x10
3. High-intensity In situ, real-time 80 K 20x20
High-pressure Micro samples 80 K 20x20
Direct geometry-I**) General purpose 80 K 20x20
Inverse geometry Molecular systems 80 K 20x20
7. Magnetic Magnetic structure 30 K 20x20
8. Direct geometry-II***) General purpose 30 K 20x20
9. Energy dispersive Complex media 30 K 20x20
*) Fourier chopper **) Fermi chopper ***) Set of choppers
10. High-resolution General purpose 30 K 10x10
11. High-intensity-I In situ, real-time 30 K 10x10
12. High-intensity-II Micro samples 30 K 10x10
13. Horizontal plane General purpose 30 K 10x10
14. Vertical plane Liquid media 30 K 10x10
15. “White” beam General purpose 30 K 10x10
2
4
3
6
*) report A. Balagurov
4
8
8
10+2

## Slide 33: Results and deliverables

## Slide 34: Stages
Scientific rationale for a new source, "white book";
Development and justification of the choice of the conceptual design of a high-flux pulsed neutron source of periodic operation;
Preparatory work for the development of production technology for fuel/target for the new source;
Development of the concept of arrangement of neutron moderators, extracted neutron beams and instruments;
Preparation of initial data and specifications for the development of a technical design of the source with research instruments on extracted neutron beams.

## Slide 35: Expected results
Feasibility study for construction of a new neutron source: document with conceptual design review;
Scientific rationale:
  Scientific program;
  Suite of instruments for condensed matter research;
  Instruments for experiments in nuclear physics;
Initial data and specifications for the design of the new source with a suite of research instruments on extracted beams;

## Slide 36: Resource requirements

## Slide 38: Conclusion

## Slide 40
Thanks a lot for your attention!