## Slide 1
4th BM@N Collaboration meeting, October 14-15, 2019
A. Ivashkin
INR, Moscow
Integration of new FHCAL and Forward Hodoscope

## Slide 2
FHCal at BM@N
Central hole for high intensity ion beam.
Central part – 34 MPD-like modules with 15x15 cm2 transverse sizes. Longitudinal segmentation - 7 sections.
Outer part – 20 CBM modules with 20x20 cm2 transverse sizes. Longitudinal segmentation – 10 sections.
Previous ZDC is replaced by new FHCal .

## Slide 3
Assembly of the FHCAL (Sep. 2019)
Front view of FHCal
FHCal is already in BM@N experimental area!

## Slide 4
Assembly of the FHCAL (Sep. 2019)
FEE of FHCal - already installed.
MPD module - 7 channels;
CBM module – 10 channels;
Photodetectors – MPPCs;
two-stage amplifiers;
HV channels;
LED calibration source.
Optical connectors

## Slide 5
Slow Control of FHCal - in progress.
Control of HV at photodetectors (MPPC);
Temperature control of photodetectors;
Compensation of temperature drift of MPPC gain;
Monitoring of MPPC gain with stabilized light source.
SC System module
LED stabilized source

## Slide 6
Readout of FHCal – to be done.
The readout electronics: FPGA based 64 channel ADC64 board, 62.5MS/s (AFI Electronics, JINR, Dubna).
One ADC board for 9 central modules
or
One ADC board for 6 outer modules
Requested:
8 ADC boards;
Cooling of ADC boards;
Power supply for 8 ADC boards;
Remote control on power supply;
Data Acquisition.

## Slide 7
Data Flow from FHCal.
Number of ADC readout channels – 440;
Number of samples per one ADC channel – 100;
Size of one ADC sample – 2 Bytes;
Size of one event: ~100 kB;
Trigger rate ~ 105.
FHCal Data Flow - 10 MB/sec.
Minimum 20 ADC samples are needed to digitize the signal.
About 100 ADC samples are needed to reject the pile-up.
Occupancy ~100% for heavy ion beam.

## Slide 8
Forward Hodoscope in FHCal beam hole – in development
quartz strips 5x80x3 mm.
Light readout by Hamamatsu MPPC.
PCB with 30 SiPMs
PCB with 30 SiPMs
ADC
30x2=60 quartz strips;
5x80x4 mm3;
It covers beam hole 15x15 cm2.
One ADC board is needed.
Slow control and DAQ would be the same as for FHCal.

## Slide 9
Summary and open issues.
Next year FHCal and Forward Hodoscope must be integrated to BM@N setup.
Data Acquisition is the most sensitive issue.
9 ADC boards and power supplies are needed.
Cooling system.
Integration to general DAQ.
Trigger? Centrality – FHCal? Minimum bias - Forward Hodoscope?
Collaboration with other detector groups is strongly appreciated!

## Slide 10
Thank you!