## Slide 1
Создание первой очереди
центральной трековой
системы установки BM@N
А.В. Галаванов, С.Е. Васильев†, Е.М. Кулиш, М.Н. Капишин, А.М. Маканькин,
А.И. Максимчук, С.В. Хабаров

## Slide 2
BM@N experiment
The basic requirements for the tracking system are:
- capability of stable operation in conditions of high loadings up to 105 Hz/cm2;
- high spatial and momentum resolution;
high geometrical efficiency (better than 95%);
maximum possible geometrical acceptance within the BM@N experiment dimensions;
- tracking system detectors must function in a 0.8 T magnetic field.

## Slide 3
BM@N GEM 1632x450 mm2 chambers
0.8
0.68
0.16
0.8

## Slide 4
cathode
magnetic field – 0.5 T
GEM3
anode
GEM2
GEM1
Chart: Space resolution vs magnetic field and track angle
| -45 | -30 | -15 | 0 | 15 | 30 | 45
B=0.0 T | 393 | 246 | 107 | 18 | 110 | 303 | 398
B=0.25 T | 346 | 214 | 84 | 40 | 151 | 311 | 418
B=0.5 T | 269 | 181 | 64 | 81 | 207 | 353 | 445
Simulation of electron shift in
magnetic field
Chart: Center gravity shift vs magnetic field
| 0 | 0.25 | 0.5
 | -0.008 | 0.395 | 0.779
Electrons drift due to magnetic field (Garfield & Maxwell simulations)
Ar(70)/CO2(30) gas mixture

## Slide 5
GEM assembly at CERN Workshop
Readout board preparation
Gluing of the readout boards
on the honeycomb support plane
Right readout board

## Slide 6
GEM assembly at CERN Workshop
Base plastic frame
GEM foil preliminary
stretching
GEM foil tests

## Slide 7
GEM assembly at CERN Workshop
Nuts in plastic frames
Brass fitting
Stack of 3 GEMs
Cathode plane

## Slide 8
GEM assembly at CERN Workshop
Stretching process
Assembled
GEM
chamber
HV divider

## Slide 9
GEM 1632x450 mm2 response uniformity
Response uniformity 3D plot of three 1632x450 mm2 chambers, Ar(90)/Isobutane(10) gas mixture
Gas gain distribution normalized on average gas gain for three 1632x450 mm2 chambers, Ar(90)/Isobutane(10) gas mixture

## Slide 10
GEM Optimization
Working point
- Working range of field, kV/cm (Ar(70)/CO2(30)gas mixture)

## Slide 11
GEM Optimization
(Ar(90)/IsoButane(10) gas mixture)
Lambda summary = 0.86

## Slide 12
GEM gas gain measurements
Amplitude distribution, Ar(70)/CO2(30), Fe55
GEM gas gain for Ar(70)/CO2(30) and Ar(90)/Isobutane(10) gas mixtures
cathode
Gem1
Gem2
Gem3
anode
Fe55
Discr.
Trigger
ADC
Experimental
scheme

## Slide 13
GEM Electronics
 | VA162 | VA163
Number of channels | 32 | 32
Input charge | -1.5pC ÷ +1.5fC | -750fC ÷ +750fC
Shaping time | 2÷2.5µs | 500ns
Noise | 2000e ENC at 50pF load | 1797e ENC at 120pf load
Linearity positive charge | 1% | 0.5%
Linearity negative charge | 3% | 1.4%
Gain | 0.5 µA/fC | 0.88µA/fC
Total power max. | 66mW | 77mW
Stand was developed for tests of FEE characteristics. More than 500 FEE were tested.

## Slide 14
GEM occupancy for different sectors design
GEM X strips occupancy
GEM vertical and horizontal foil sectors

## Slide 15
GEM cosmic tests
Cosmic stand
GEM residuals vs track angle
GEM geometrical efficiency

## Slide 16
GEM configuration
GEM tests at Nuclotron deuteron beam
X
Z beam
target
GEM 66x41cm2, 5 planes
GEM 163x45cm2, 2 planes
Si
The average trajectories of the deuteron beam and the average Lorentz shifts of an electron avalanche in 6 GEM planes measured for four values of the magnetic field.
GEM efficiencies

## Slide 17
GEM central tracking system performance
at Ar and Kr beams (March 2018)
Example of the event reconstruction
in the central tracker in Ar+Al interaction
Seven GEM 1632x450 mm2 chambers produced
at CERN workshop were integrated into BM@N experimental setup.
Pile-up suppression in Ar, Kr runs: 3 µs before and 0.5 µs after trigger signal
GEM X&Y amplitude distributions
Amplitude, ADC counts
Amplitude, ADC counts
Fragments of Ar beam in one
of the GEM chambers

## Slide 18
GEM tests at Nuclotron d, C, Ar beams
GEM hit residuals, magnetic field 0.79 T,
Ar(90)/IsoButane(10), deuteron beam
σ x = 127 um
GEM hit residuals, w/o magnetic field,
Ar(90)/IsoButane(10), deuteron beam
GEM hit residuals, magnetic field 0.59 T,
Ar(70)/CO2(30), carbon beam
GEM hit residuals, magnetic field 0.6 T, Ar(80)/Isobutane(20), Ar beam, Edrift = 1.5kV/cm

## Slide 19
Для успешной интеграции детекторов в состав экспериментальной установки были:
- разработаны online программы обработки информации с детекторов, позволяющие оценить качество получаемых данных как на пучке ускорителя, так и от радиационного источника;
- разработаны программы медленного контроля низковольтного и высоковольтного питания детекторов с передачей данных в базу данных («Tango»);
- разработана и собрана система подвески детекторов в магните СП-41 с возможностью юстировки детекторов;
разработана и собрана система подачи и контроля газовой смеси.
Первая очередь центральной трековой системы представляет собой:
- 7 детекторов размером 1632×450 мм2,
- 5 м2 активной площади,
- ~ 750 миллионов независимых каналов газового усиления,
- ~ 45000 каналов считывающей электроники,
более 1.5 км кабелей управления и считывания информации.
Трековая система успешно работала в сеансах Нуклотрона на пучках дейтронов, углерода, аргона и криптона. В результате были получены важные данные по трековым характеристикам детекторов в магнитном поле и по импульсному разрешению для частиц пучка. Это позволило восстановить сигналы распадов гиперонов, рожденных при взаимодействии пучков Нуклотрона с фиксированными мишенями.
GEM детекторы с активной областью 1630×450 мм2 в настоящее время являются самыми большими GEM детекторами в мире.
Заключение

## Slide 20
Thank you for
your attention!

## Slide 21
Back-up slides

## Slide 22
Electric field in the region of the holes of a GEM electrode
Electron microscope picture of a section of typical GEM electrode, 50 μm thick. The holes pitch and diameter are 140 and 70 μm, respectively.
Schematics of single GEM detector with Cartesian two-dimensional strip readout.
The gas electron multiplier (GEM)
DRIFT
INDUCTION

## Slide 23
GEM HV divider scheme
I, mkA | DR, kv/cm | G1, v | TR1, kv/cm | G2, v | TR2, kv/cm | G3, v | IND, kv/cm
370 | 0.88 | 303.4 | 1.92 | 288.6 | 2.78 | 273.8 | 3.16
490 | 1.17 | 402 | 2.58 | 382 | 3.68 | 363 | 4.18
370 mkA – working point for Ar(90)/Isobutane(10) gas mixture
490 mkA – working point for Ar(70)/CO2(30) gas mixture
50 kΩ
715 kΩ
820 kΩ
1.3 MΩ
780 kΩ
1.5 MΩ
740 kΩ
1.28 MΩ
2000 pF
HV