## Slide 1: FHCal Slow Control Integration
O.Petukhov
INR RAS, Moscow

## Slide 2
FHCAL
FHCAL consists of 2x44 modules of ~1.1x1.1 m2 each part.
The Forward Hadron Calorimeter in MPD setup
7 analog channels in each module

## Slide 3
Front-End-Electronics
Board with SiPMs
Board with FEE
MPPC
Integrator
ADC
τ ~ 20ns
Amp
FEE
Dt ~ 50 ns
Dt ~ 200 ns
Connector for analogue signals
Connector for slow control
44x7= 308 channels on each side.
Or 608 channels for full calorimeter
LED
4 pins in each module
S

## Slide 4: SC System Module position and cable routing
SM
At least one Slow Control System
Module is needed for each side
Needs 220 V AC power
RJ-45 Ethernet cable for network connection
(alternative: connection to a PC
via RS232 )
Slow control

## Slide 5: Slow Control Network
SM
Serial RS485-based protocol with 10-pin flat cable from System Module to FEE
Serial over TCPIP from PC to System Module(s)
Software to control HV, LED calibration

## Slide 6: Slow Control Integration
Software connected directly to System Module or via proxy (Socket manager)
Other clients (database loggers, etc.) can connect to Socket Manager
More variables?

## Slide 7: Backup slides

## Slide 8: Front-end electronics connections
To Slow Control:
10 wire ribbon cable
LED flash trigger (optional):
50 Ohm coaxial cable
Analog sum output:
50 Ohm coaxial cable
To ADC:
8-pair flat cable

## Slide 9: Slow Control System Module connections
220 V AC Power
LAN connection:
Ethernet cable with RJ-45 connector
To Front-end modules:
10 wire ribbon cable

## Slide 10: ADC connections
12 V 2A DC Power:
2X3 MF pin connector
Trigger TTL input
Xoff TTL output
2X 50 Ohm coaxial cable
Data readout & White Rabbit synchronization:
2X SFP modules

## Slide 11: Optional connections
44 coaxial 50 Ohm cables to LED trigger on modules

## Slide 12: Slow Control
At least one Slow Control System Module is needed for each side
Needs 220 V AC power
RJ-45 Ethernet cable for network connection (alternative: direct connection to a PC via USB (unstable) or RS232 (DB-9))

## Slide 13: ADC
At least 5 ADC64 boards needed on each side
Each board needs 12 V DC power supply capable of sourcing at least 1.5 A of current, preferably DC regulated power supply with remote control capabilities and output current of 2 A per channel
Network connections for DAQ and WR
Coaxial cables for trigger distribution and busy logic
Cooling