## Slide 1
BEAM TRANSFER CHANNELS,
INJECTION AND EXTRACTION SYSTEMS
Tuzikov A.

## Slide 2
NICA beam transfers
Beam transfer from HILAC to Booster
HILAC-Booster transport channel;
Booster injection system.
Beam transfer from Booster to Nuclotron
Booster fast extraction system;
Booster-Nuclotron transport channel;
Nuclotron high energy beam injection system.
Beam transfer from Nuclotron to Collider
Nuclotron fast extraction system;
Nuclotron-Collider transport channel;
Collider injection system.
Beam dump from Collider
Collider beam dump system.
NICA MAC 2017

## Slide 3
Beam transfer from HILAC to Booster
Goals
Accumulation of required intensity of ions in Booster by means of several methods of beam injection.
Beam parameters
Ions | Au31+
Energy, MeV/u | 3.2
Magnetic rigidity, T m | 1.6
Electric rigidity, MV | 40
Ion number | 2∙109
HILac
Booster
NICA MAC 2017

## Slide 4
The beam transport with minimal ion losses.
The beam debunching.
The beam matching.
Separation and adsorption of neighbor charge states of ions.
Providing different schemes of the beam injection into the Booster.
Main goals
HILAC-Booster beam transport channel
Beam transport in the median plane of the Booster.
The debuncher in non-dispersive region of the beam transport channel.
Features
NICA MAC 2017

## Slide 5
Parameters of main elements
HILAC-Booster beam transport channel
Quadrupoles
Effective length, m | 0.29
Max gradient, T/m | 10
Gap (diameter), mm | 95
Available at JINR
Dipoles
Effective length, m | 0.65
Max field, T | 1
Gap, mm | 45
Debuncher
Designed and fabricated by Bevatech team
Inner length, m | 0.49
Frequency, MHz | 100.625
Max effective voltage, kV | 260
NICA MAC 2017

## Slide 6
HILAC-Booster beam transport channel
Beam dynamics
Separation
Beam envelopes
Horizontal and vertical acceptances of the channel are equal to 35 π·mm·mrad.
Reducing from 5·10-3 to 1·10-3 by means of the beam debunching.
NICA MAC 2017

## Slide 7
IK1
IES
IK2
IK3
The beam injection with minimal ion losses.
The beam injection by the following methods: single-turn injection, multiturn injection, multiple injection.
Goals
Booster injection system
Accumulation of ions in horizontal phase plane.
Closed orbit bump (for multi-turn and multiple injections).
Rapid change of fields in the system elements (for more compact filling of the horizontal phase plane in case of multi-turn and multiple injections).
Features
NICA MAC 2017

## Slide 8
Parameters of elements
 | Length, m | Gap, mm | X1, mm | X2, mm | Max voltage, kV
IK1 | 0.5 | 100 | -50 | +50 | 40
IK2 | 0.8 | 93 | -36 | +57 | 50
IK3 | 0.5 | 100 | -50 | +50 | 60
IES | 1.9 | 35 | [+38; +195] | [+73; +230] | 125
Booster injection system
Electrostatic septum IES
Electric kicker IK1
NICA MAC 2017

## Slide 9
Goals
Transfer of the beam with parameters which can be altered in wide ranges due to 1) use of different schemes of beam injection into Booster and 2) use of an electron cooling system.
Ion stripping to a maximum charge state.
Ions: before stripping station after stripping station | Au31+ Au79+
Maximum magnetic rigidity of ions, T m: before stripping station after stripping station | 25 10
Ion number | 1.5∙109
Beam Parameters
Beam transfer from Booster to Nuclotron
Booster
Nuclotron
NICA MAC 2017

## Slide 10
Parameters of elements
Length, m | 1.5
Max magnetic field, T | 0.18
Bending angle, mrad | 10
Pulse duration, μs: rise plateau | 0.5 0.5
Booster fast extraction system
Kicker
Length, m | 0.4; 1.4
Max magnetic field, T | 0.5; 1.3
Bending angle, mrad | 20; 185
Pulse shape | semisinusoidal
Pulse duration, μs | 80; 1200
Septum (two sections)
NICA MAC 2017

## Slide 11
Kicker
Booster fast extraction system
Initial version
NICA MAC 2017

## Slide 12
Asymmetric (being designed by BINP team)
Kicker
Booster fast extraction system
1 – the kicker conductors; 2 – the vacuum box of the kicker;
3 – the circulating beam; 4 – the extracting beam;
5 – the vacuum chamber at the entry and the exit of the kicker.
NICA MAC 2017

## Slide 13
Booster fast extraction system
Beam extraction
NICA MAC 2017

## Slide 14
Goals
The beam transport with minimal ion losses.
Separation of neighbor charge states. Estimates of ion stripping at energy of 580 MeV/u: 100% Au31+ → 80% Au79+, ~20% Au78+. Due to high intensity of Au78+ ions they have to be extracted from the channel to an absorber.
Booster-Nuclotron beam transport channel
View from above
Side view
NICA MAC 2017

## Slide 15
Booster-Nuclotron beam transport channel
Preliminary parameters of magnetic elements
Magnetic element | Type | Effective length, m | Max. magnetic field (gradient), T (T/m)
BM1 – BM5 | sector dipole | 2 | 1.7
SEPT_2 | septum | 1.5 | 1.35
Q1 – Q8 | quadrupole | 0.4 | 16
NICA MAC 2017

## Slide 16
Booster-Nuclotron beam transport channel
Beam dynamics
NICA MAC 2017

## Slide 17
Nuclotron high energy beam injection system
Preliminary parameters of elements
Length, m | 2
Max magnetic field, T | 0.1
Aperture, mm×mm | 110×70
Pulse duration, μs: rise plateau fall | ≤ 0.5 ≥ 0.5 ~10
Kicker
Length, m | 1.5
Max magnetic field, T | 1.1
Septum thickness, mm | 7
Power supply | DC
Lambertson magnet
NICA MAC 2017

## Slide 18
Magnetic elements
Nuclotron high energy beam injection system
Kicker
Lambertson magnet
NICA MAC 2017

## Slide 19
Beam transfer from Nuclotron to Collider
Goals
Alternate filling of the Collider rings.
Accumulation of required intensity of ions (with help of barrier bucket system and beam cooling systems of Collider).
Ions | Au79+
Energy of ions, GeV/u | 1 ÷ 4.5
Magnetic rigidity of ions, T m | 14 ÷ 45
Ion number | 1∙109
Beam Parameters
NICA MAC 2017

## Slide 20
Nuclotron fast extraction system
Preliminary parameters of elements
Length, m | 3
Max magnetic field, T | 0.13
Aperture, mm×mm | 110×70
Pulse duration, μs: rise plateau fall | ≤ 0.7 ≥ 0.2 ~10
Kicker
Length, m | 0.5; 2.5
Max magnetic field, T | 1; 1.6
Septum thickness, mm | 5; 10
Power supply system | cyclic, serial to dipole magnets
Lambertson magnet (two sections)
NICA MAC 2017

## Slide 21
Beam extraction
Nuclotron fast extraction system
The beam shift to the septum by means of RF system: = 1.4·10-2.
The kick in horizontal plane: angle 7 mrad.
The beam deflection in vertical direction: angle 100 mrad.
NICA MAC 2017

## Slide 22
Goals
Nuclotron-Collider beam transport channel
The beam transport with minimal ion losses.
The beam matching with lattice functions of the Collider rings (except vertical dispersion).
NICA MAC 2017

## Slide 23
Parameters of pulsed magnet elements
Nuclotron-Collider beam transport channel
Magnetic element | Number | Effective length, m | Max. magnetic field (gradient), T (T/m)
Long dipole | 21 | 2 | 1.5
Short dipole | 6 | 1.2 | 1.5
Quadrupole Q10 | 25 | 0.333 | 30
Quadrupole Q15 | 8 | 0.5 | 30
Steerer | 40 | 0.4 | 0.11
Designed by SigmaPhi
NICA MAC 2017

## Slide 24
Beam dynamics
Nuclotron-Collider beam transport channel
NICA MAC 2017

## Slide 25
Length, m | 4.5
Max magnetic field, T | 0.1
Aperture, mm×mm | 80×60
Pulse duration, ns: total plateau | 700 150-200
Kicker
Preliminary parameters of elements
Collider injection system
Length, m | 2.5
Max magnetic field, T | 1
Aperture, mm×mm | 45×45
Septum thickness, mm | 3
Pulse shape | semisinusoidal
Pulse duration, μs | ~ 10
Septum
NICA MAC 2017

## Slide 26
Septum
26
Booster fast extraction system
NICA MAC 2017

## Slide 27
Collider injection system
Kicker with correcting conductors
Magnetic fields in kicker conductors
plateau
± 2.5%
NICA MAC 2017

## Slide 28
Beam dump directions
Collider beam dump system
NICA MAC 2017

## Slide 29
Beam dump from upper ring
Collider beam dump system
NICA MAC 2017

## Slide 30
Beam dump from lower ring
Collider beam dump system
NICA MAC 2017

## Slide 31
THANK YOU FOR ATTENTION