## Slide 1: An upgraded TOF-ΔE1-ΔE2-E (DSSSD) based spectrometer for heavy-element research at the Dubna Gas-Filled Recoil Separator
1. Introduction. Synthesis of SHE at the DGFRS.
2. DGFRS, detection system, real-time algorithm to search for ER-α sequences.
Experiment 240Pu +48Ca->*Fl + some another examples of method of “active correlations” application
( in part : NEC’2015 & MMCP’2017)
3. (nearest future ~end 2017-18) Ultra high beam intensities (specifics)
(JINR, FLNR DC-280 project). ~5-10 pμA 48Ca, 50Ti..!
+reasonable scenarios
4. Summary
Yu.S.Tsyganov, A.N.Polyakov, A.A.Voinov, L.Schlattauer, M.Shumeiko
FLNR, JINR +
@Collaboration Dubna-Livermore-Oak Ridge (JINR-LLNL-ORNL)
tyra@jinr.ru , +7-4962167590
Table of contents
NEC’2017
Montenegro, BUDVA
SEPT. 26
President IUPAC
Prof. Tarasova
Russia Federation Science & Education
Minister Mrs. Vasilieva
Pesentation of discoveries Z=115,117,118
Elements in Moscow scientific club

## Slide 2: SHE synthesis : the DGFRS results

## Slide 3
Gas-Filled Recoil Separator
New FPD:
48 by 128 strips (48*128 mm2) DSSSD,
6*(48*128 mm2) side detectors + 1 “veto”
And two independent registering
systems

## Slide 4: Calibration process
217Th (T1/2 = 237 µs )
natYb+48Ca217Th+3n
217Th
(main)
DSSSD
September 15 /2015

## Slide 5
What is correlation?
Energy-time-position –TOF-ΔESTART,STOP
0 – Alpha-like
EVR - like
background
Typical spectra
time

## Slide 6
General philosophy of “active correlations” method
Correlation : 3D+1 (in our case) = energy-position(x,y)- time. If to “kill” (=localize) e-(x,y)  it will be very simple structure (~one dimensional)
+1 means that whether TOF || ΔE 1,2 > 0 or both parameters =0 (EVR like or alpha-like signals)
t  elapsed time from electronics
correlation YES!
Required but not sufficient condition
…but, it is not our goal !
In PC memory to transform to:
Correlation graph (Def)
Where an is an appropriate
||tn||- T matrix  an
with tn k,m element as an elapsed time.
k,m indexes are correspond horizontal and vertical strip numbers, respectively
smart (def. )
except…
Radical beam ass.
background suppression!
Results in
for a short time
Beam stopEVR *(α1+α2+...)
1)
2) Integrated system should be
DAQ, control system – the same standard
// not necessary, but preferable!
J(cyclotron) = 1 pμA, if no pointer
= 0, if pointer to correlation YES
N(N-1)/2 graph edges
If N- number of nodes
!!!

## Slide 7
Method of “active correlations”
//New – 17 mcS ( fifo internal memory 8 X2.5 μS)
Time-energy-position correlation ER-alpha detected in a real-time mode
Provides beam stop for a short time. In the case of detecting next alpha decay signal in the same position “beam-off” interval is prolonged for a few times. Beam interrupting is performed at the position of injection line ( ~ 18 kV )
Yu.S.Tsyganov // J. Phys. G: Nucl. Part. Phys. 25(1999) 937-940
Yu.Tsyganov & A.Polyakov// Appl. Rad. &Isotopes v.47 No.4(1996)451-454
Moreover modern versions are: Yu.Tsyganov et al. NIM A525(2004)213; A513(2003)413; A558(2006)329

## Slide 8: Synthesis of neutron-deficient isotopes
240Pu+48Ca reaction
Target 0.49 mg/cm2
Energy of 48Ca 245 MeV
Excitation energy 36.5 – 41.1 MeV
Beam dose 4.0*1018
s3n = 2.5 pb
+2.9
-1.4
Example #1
2016-2017

## Slide 9
Yu.Oganessian et al.
PRC 87, 054621(2013)
Example #2
249Bk+48CaTs*
Isotopes 249Bk and 249Cf were produced in ORNL (USA)
By 250 days irradiation of targets Cm and Am
With thermal neutrons flow 2.5  1015 n/cм²·с of HFIR reactor
HFIR reactor of ORNL
Rotating target
design
22 mg pure Bk
Target wheel..
WR !
WR !

## Slide 10
SHE-factory: High-current cyclotron DC280
DC280 (expected) E=4÷8 MeV/A |  | 
Ion | Ion energy [MeV/A] | Output intensity
7Li | 4 | 1×1014
18O | 8 | 1×1014
40Ar | 5 | 6×1013
48Ca | 5 | 0,6-1,2×1014
54Cr | 5 | 2×1013
58Fe | 5 | 1×1013
124Sn | 5 | 2×1012
136Xe | 5 | 1×1014
238U | 7 | 5×1010
Main setups:
DGFRS (synthesis), GFS (chemistry), SHELS
Main tasks:
Synthesis of SHE.
Properties and Spectroscopy of SHE;
Chemistry of SHE;
Searching for new reactions leading to SHE
High voltage injection system
(2 platforms)
48Ca, 50Ti ~ 5-10 pµA
If tomorrow comes

## Slide 11
The main building of the SHE-Factory
(May 2017)
11.09.2015

## Slide 12
The hall of DC-280 of the SHE-Factory

## Slide 13
Basic improvements in a nearest future
“TekhInvest” ADP-16 1M CAMAC+ high integration unit
- 16 in from 16 out preamp
- two scales (alpha + FF)
- 8 x 2.5 μS hash internal memory (with time stamps),
i.e. sequence like 2.5-2.5-2.5-2.5-2.5-2.5-2.5-2.5 μS is detectable
(~15-17 μS regular dead time)
2) More extended RT algorithms
3) First test at alpha particle source in 2017 April – June…
ADP-16 1M unit (“TekhInvest”, free economy zone “Dubna”)
48(fr) +128(bc)+48(s) =224 div 16= 14 units

## Slide 14
dT=2.5x8 + 25x8=220 μS for ν=103 Hz
λ=220 x10-6 x 103 =0.22
where
P(>9) =2.7 e-12
Therefore: dead time t(dead) = 2.5 µS with probability 1- P(>9)
= 25 µS 2.7e-12

## Slide 15
New version for “active correlations” method
PC
Totally : 48+128+3+7= el. channels.. 128 without amplitude (7+2 ) bits info
Windows XP

## Slide 16
DSSSD Micron Semiconductors (UK) –ORNL (USA, TN) application
Main advantage – lover area of “elementary” cell (~1/10 83% cases !) and
(significantly for the method of “ AC”) – practically ready ER matrix for use.
But… from p-n junction side (back)  edge effects between the neighbor strips
~10% (α 5.5 МeV, close to 2π geometry) 128 strips.
(as to ohmic contact side) edge effect is suppressed due to  P+ separation guard layer
( Dr. Susanne Welsh, Micron Scd’s , UK// 2014. private comm. // ~ 0.1% ORNL
Front side.
______________________________________________________
Yu.Tsyganov Lett. to ECHAYA 2015. v.12, no.1(192) 128-135, v.12 no.4 (195), pp.885-894
& Cybernetics and Physics 2014. No.3 . Pp.85-90
~0.1% sharing
~10% α-source 5.5 MeV ; close to 2π geometry
a
b
(el. Field) Fa < F b
As a result 

## Slide 17
Neighbor strips edge effect ( from p-n side)
energy=0; enb=0; enb1=0; enb2=0;
if (strip>=0 &&strip< 48) energy = (aa[strip]*float(wa)) +bb[strip];
if (strip_1 >=0 && strip_1 < 128) enb1=EAB1[strip_1]*float(wab) +EAB0[strip_1];
if (strip_2 >=0 && strip_2 < 128) enb2=EAB1[strip_2]*float(wab) +EAB0[strip_2];
enb = enb1+enb2+ballistic_dfc;
// ----------- начинаем фильтровать begin filtering --------------------------------
EVR=false; ALFA=false;
if (tof > TOF_MIN && tof < TOF_MAX && energy > ER_MIN && energy <=ER_MAX ) EVR = true;
if (tof==0 && energy > MINALFA && energy < EA_MAX) ALFA= true;
if (fabs(energy-enb) > D_ENERGY) ALFA=false;
State register (positional code, test)powers of 2 – single signal
C++ program fragment
Extracted via ER-alpha
Ballistic dfc~29 KeV=0.3%
In average!
Test for distance alpha source
Test June
2017
% of double signals
From p-n side
Q1(t)
Q2(t)
! Of course: r1,2 = f (V)
p-n junction side
Ballistic Deficit
See: A.Doehring et al.
NIM 59(1968)49

## Slide 18
Where:
,
and
C – capacity top strip rel bot strip Cpix << C << C str (to a first appr-n, roughy –
And i(t)- is an incoming function variable.
Common solution
R 1,2 = R(Voltage)

## Slide 19
…OR ( in a numerical form of solution..)
h << TP
..taking into account that…
i(t) – incoming function

## Slide 20
What is Tp (plasma time)
W.Seibt, K.E.Sundsroem and P.A.Tove
NIM 113(1973)317-324
SCLC track
destruction model
FEFF << F
P+
N+
……….
100 µm

## Slide 21
SUMMARY: NEC’2017, Budva
.
Since beginning of the millennium six new superheavy elements and more than 50 new isotopes of the heaviest elements were synthesized for the first time at our Laboratory employing one and only experimental setup -- the Dubna Gas-filled Recoil Separator.
It was namely method of “active correlations” which allowed to detect decays of superheavy nuclei in fact in background free mode
3) “AC” method is extended for DSSSD.
First experiment 240Pu+48Ca *Fl is successfully finished.
Prototype of new GFS-2 (DC-280 project) smart detection system (incl. software) is designed and successfully tested at U-400 main FLNR cyclotron HI beam and alpha particle source . Upgraded version will be applied in December 2017 experiment at U-400 cyclotron
Simple version of equivalent circuit neighbor strip model is proposed
I plan to report it in a more sophisticated form at MMCP’2019 will held in Stara Lesna, Slovakia in 2019
DGFRS
1st team
~ 1993
New gas-filled separator( project )
~2018

## Slide 22
Flerov Laboratory of Nuclear Reactions, JINR, Dubna
THANK YOU
FOR YOUR
ATTENTION!
Nearest future plans ~ 1st December 2017 : 244Pu + 50Ti  Lv*
 if it will be 1 event or even more(!)
in month or two then Cf+Ti120* for a few months..
If null effect  till new separator will put into operation at DC-280 super intense
FLNR cyclotron…Taking into account: -TASCA - cross sections -rot. target design…etc. =
It is not a problem “how to obtain”
(high intensity beam, but, it is the problem “ how to apply”!
 step by step as a reasonable scenario.