## Slide 1
Instrumentation and moderators at long pulse neutron sources
JINR PAC
Jan. 25, 2019
F. Mezei
Technical coordinator, ESS ERIC
Prof. emeritus, HAS Wigner RC.
www.europeanspallationsource.se

## Slide 2
RFast neutrons are (energy) expensive
Fast neutrons produced / joule heat deposited:
Fission reactors: 3x1010 (in  50 liter volume)
Spallation (> 400 MeV): 2x1011 (in  2 liter volume)
  Fusion: 4x1011 (in ~ 2 liter volume)
  (but neutron slowing down efficiency reduced by ~20 times)
  Electron accel.: (50 MeV) 2x109 (in  0.01 liter volume)
Low energy p.: (5 MeV): 2x108 (in  0.001 liter volume)
(35 MeV): 2x109 (in  0.01 liter volume)
Laser induced fusion: ~ 104 (in ~ 10-9 liter volume)
Energy costs are important: 20 % of staff costs at ESS in operation
From 1 000 000 fast neutron produced: ~1 ends up in the beams

## Slide 3
Part of spectrum used by a diffractometer for large structures (e.g. biological membranes)
continuous source

## Slide 4
Part of spectrum used by a D22 (ILL) class instrument (Small Angle Neutron Scattering)
continuous source

## Slide 5
Part of spectrum used by a SANS instrument
continuous source 50 Hz pulsed source
PPulsed neutron sources: born in Dubna
More efficient use of neutrons produced

## Slide 6
Part of spectrum used by a D22 (ILL) class instrument
16 Hz pulsed source
continuous source 50 Hz pulsed source

## Slide 7
Part of spectrum used by a D22 (ILL) class instrument
16 Hz pulsed source
continuous source 50 Hz pulsed source
Efficiency gain by pulsing:  / ~8-100

## Slide 8
Part of spectrum used by a D22 (ILL) class instrument
16 Hz pulsed source
continuous source 50 Hz pulsed source
Efficiency gain by pulsing:  / ~8-100
Substantial overall progress beyond continuous sources in cold neutron research (soft matter, nanoscience): need to surpass their time average flux in low repetition rate (10 – 20 Hz)

## Slide 9
ESS pre-history
Steel
shielding
Monolith
liner
(Mezei, 1994)
1992: 100 kJ short pulses, two target stations
1993: add 400 kJ long pulses
2006: ESFRI road map call: one target station, long pulses, 5 MW

## Slide 10
Variety of different lay-outs, e.g. SNS
Instantaneous power on target (for 1 MW at
60 Hz, i.e. 17 kj in ~1 s pulses on target): 17 x

Short pulses spallation sources: current generation
1 GW

## Slide 11
Cost equivalent linear accelerator alone can produce the same cold neutron pulses by ~100 s proton pulses at ~ 0.15 GW instantaneous
power
simplify
15 kj/pulse

## Slide 12
If we find ways to control pulse parameters by neutron beam choppers (pulse length, repetition rate):
 Leave the linac on for more neutrons per pulse and higher peak brightness (Long Pulse source)
simplify
300 kj/pulse
Cost equivalent linear accelerator alone can produce the same cold neutron pulses by ~100 s proton pulses at ~ 0.15 GW instantaneous
power
0
500
1000
1500
2000
2500
3000
0,0
2,0x10
13
4,0x10
13
6,0x10
13
8,0x10
13
1,0x10
14
1,2x10
14
1,4x10
14
1,6x10
14
Instantaneous brightness [n/cm
2
/s/str/Å]
Time [
m
s]
Enhancement by simplifying

## Slide 13
If we find ways to control pulse parameters by neutron beam choppers (pulse length, repetition rate):
 Leave the linac on for more neutrons per pulse and higher peak brightness (Long Pulse source)
Higher peak flux than short pulses for equal costs!!
simplify
300 kj/pulse
Cost equivalent linear accelerator alone can produce the same cold neutron pulses by ~100 s proton pulses at ~ 0.15 GW instantaneous
power
Enhancement by simplifying

## Slide 14
Steel
shielding
Monolith
liner
J-PARC (2011)
BER-II (reactor)
Neutron beams with mechanical choppers (since Fermi, 1940s)

## Slide 15
Multiplexing system: fills in dead time by multiplying simplex uses  dissimilar sub-frames within one source frame
detector
Different instruments require different pulse rates: Repetition Rate Multiplication (also indispensable for short pulse sources)
Time-of-flight spectroscopy:

## Slide 16
Multiplexing system: fills in dead time by multiplying simplex uses  dissimilar sub-frames within one source frame
detector

## Slide 17
(Nearly) free choice of pulse repetition rate for TOF spectroscopy, (nearly)
independently of source frequency: key to source design optimization
240 Hz data collection at 20 Hz source
Simulated data, IN500 project, Lujan Center
Optimized instrument length > 50 m
First experimental implementation: emulation of pulsed source operation at
NEAT TOF spectrometer at HZB, Berlin
Evidence for significant, broad band simultaneous information over a broad range of incoming wavelengths
(length 13.5 m)
M. Russina, F. Mezei, NIMA, 2009
RRM chopper rules: fi = nfS fiLi = fjLj
fi, Li "quantized"

## Slide 18
Principle of "selective pulse suppression" chopper: synchronized at source frequency
Advanced RRM tools:
- Broad band Fermi choppers: short slit package (1-2 cm) (TOF Diffractom. EXED, HZB)
- "Magic chopper": pulse length t   (J-PARC)
- Selective pulse suppression: RRM frame length T custom designed, e.g.   M. Russina, F. Mezei, ICNS09, 2010
=0

## Slide 19
First RRM experimental data on a pulsed source instrument: 4-SAESONS
M. Nakamura, R. Kajimoto, Y. Inamura, F. Mizuno, M.Fujita, T. Yokoo, M. Arai, J. Phys. Soc. Jpn. 2009
Simple implementation by transmission band of Fermi chopper (red line) and low source frequency (40 ms source repetition rate)

## Slide 20
High resolution TOF diffractometer Budapest Neutron Center
Built in collaboration with HMI, 1998
H.J. Bleif, D. Wechsler, F. Mezei, L. Rosta
Time-of-flight diffraction:

## Slide 21
RRM in diffraction: dial-up pulse length with perfect shape
One to one relation between time at sample and chopper opening.
Shaped pulse repetition time: ~ source pulse length (0.8 – 2 ms  500 – 1250 Hz)
Wavelength Frame Multiplication
Fully all-terrain pulse shaping tool for diffraction and inverted geometry spectroscopy at (long) pulse sources:
Multiplexing chopper system with phase slewing to source: invisible for the user
Chopper system looks for neutrons to a limited time

## Slide 22
First experimental implementation of RRM diffraction
M. Russina, Gy. Kali, Zs. Santa, F. Mezei, 2010
RRM for diffraction: Wavelength Frame Multiplication

## Slide 23
Spectrum as a function of time of detection: synchronous operation
Asynchronous operation also possible by event recording ("list mode")

## Slide 24
Monitor spectra:
Spectrum as a function of neutron flight time:
asynchronous = synchronous operation (normalized by monitor)
Fringe benefits: ideal shaped short pulses with dial up length,
multiplexing invisible and verified, single pulse work possible

## Slide 25
First WFM implemented on a pulsed source instrument: J-PARC
N. Takahashi et. al, 2011

## Slide 26
Moderators for high beam intensity
Short pulse spallation sources
pulse parameters imposed by the source design and/or fixed at each beam-line

## Slide 27
BBi-spectral beam extraction:

## Slide 28
 doubles beam intensity

## Slide 29: Flat moderators offer enhanced brightness
- Thermal neutrons arriving from the surroundings are transformed into cold ones within about 1 cm of the walls of the moderator vessel
- Along the direction of these walls this intense layer of cold neutrons can be seen from the outside into depths comparable to 10 cm.
Moderators for high beam intensity

## Slide 30: Experimental confirmation at J-PARC of physics effects behind flat moderator concept
(Kai, 2004)
- Brightness distribution of cold coupled moderator performed at MLF at J-PARC in April 2015 by J-PARC-ESS team
- Preliminary results give full confirmation of the brightness distribution across the moderator: higher in target and reflector side
- Experimental confirmation of physics
principles of flat moderators
J-PARC
>99% para-H

## Slide 31
Steel
shielding
Monolith
liner
Perturbed flux increase vs. wavelength
Thermal flux: not directional, but also enhanced
- less reflector removed
- center closer to target
- …?
Conv. moderator Volume moderator

## Slide 32
Steel
shielding
Monolith
liner
Low-D xyz moderator
brightness
(depth z = 15 cm)
Directionality:
1.5 cm x 1.5 cm
tube moderator
Low dimensional para-H2 moderators:
also for reactors, etc
Directional
moderator:
shape induced

## Slide 33
“Butterfly “ bi-spectral moderator
ESS pulse shapes
 = 3 Å
h=3 cm, w=8 cm
cold moderator
TDR (2013)
Conv. mod (2010)
H2
p-H2
n
n
0
2x10
14
4x10
14
6x10
14
 = 1.1 Å
h=3 cm, w=8 cm thermal mod. optimal position
Conv. &TDR (2013)
ESS 5 MW, 3 cm flat
moderator
ESS 5 MW, TDR 2013
ISIS TS1 128 kW
ISIS TS2 32 kW
SNS 1 MW
J-PARC 300 kW
ILL 57 MW
Qualitatively new level of beam performance
“Butterfly”
bi-spectral
moderator:
cold, thermal
ESS pulse
shapes
(L. Zanini et al, ECNS, 2015)
2.6 Å

## Slide 34
ESS novelty: low dimensional moderators
“Moderator” neutron emission at various neutron energies:
heights: 15 mm 30 mm 100 mm
Cold Thermal Fast
5 – 20 meV 50 – 150 meV > 1 MeV
Thermal moderator
Cold moderator
Improved signal
to noise ratio!

## Slide 35
Steel
shielding
Monolith
liner
ILL “options” for
cold mod. at 55 cm
(F.. Mezei et al, JNR, 2014)
Moderators for high beam intensity:
also for reactors

## Slide 36: (Optical) beam delivery
Steel
shielding
Monolith
liner
Delivering illumination for beam scattering studies
Microscope (XVI. c.):
(divergence d prescribed)
 = (r,,,) d d
Brightness  is a constant
of motion along trajectories
(if no beam loss, e.g. absorption)
Optical beam delivery for high intensity on the samples

## Slide 37
Steel
shielding
Monolith
liner
Beam delivery including optics
d ~ determined by focusing
Xtal monochromator
Figure of merit: brightness
(above a minimum size)
IN20 (ILL)
“Virtual source”
for focusing monochromator
 minimizes extracted neutrons
to reduce background:
not bigger than needed

## Slide 38
Available neutrons (“phase space”)
Neutrons available: Fmdm On sample: Fsds ,  < 1
Fmdm should be > Fsds
Beam losses:
- < 100 % reflectivity of (super)mirrors, crystals
- impact angle above the (super)mirror cut-off angle
- gaps in the guide
- absorption in air, windows, imaging errors,…
“Ballistic” guides:
Feasible to 200-300 m length
Beam delivery by optics
h
d  1/h:
phase space transformation

## Slide 39: Phase space rules
Steel
shielding
Efficient beam delivery to sample
 > 60 %, if
- “good” optical design
- (super)mirror critical
angle sufficient
- available phase space
large enough
Losses in horizontal and
vertical dimensions com-
bine: asymmetric shapes
can be advantageous
(for homogeneous moderator brightness)
d = 2
Neutrons on sample: N =  () dt dF d d
Source brightness (n/s/cm2/str/Å)

## Slide 40
In neutron scattering work for a neutron source with sufficiently long source pulses the peak flux alone matters, independently of any reasonable source time structure (continuous or pulsed)
For an arbitrary source repetition rate f one will choose the instrument length L so that to assure the desired band :
L = A -1 f –1
(A=3956 Åm/s). With this L the pulse length t for the required resolution  has to be
t = A-1 L  = f -1 ( /)
The neutron flux on the sample will be given in terms of the peak source brightness function P(), beam divergence  and the efficiency factor of the beam delivery system 
 =   t f  P() d =   (/)  P() d , Independent of f
The integral is over the wavelength band  = max - min.
Peak flux theorem

## Slide 41
Chopper system looks for neutrons to a limited time: - - defines minimum efficient pulse length = about 4 times opening time of “wall” choppers (between fully closed and open)  about 0.5 ms
- effective peak of shorter pulses = average over this minimum “long pulse” length
Conclusion: what is a “long pulse”

## Slide 42
Chopper system looks for neutrons to a limited time: - - defines minimum efficient pulse length = about 5 times opening time of “wall” choppers (between fully closed and open)  about 500 s
- effective peak of shorter pulses = average over this minimum “long pulse” length
Conclusion: what is a “long pulse”
Example:
15 MW long pulse reactor
at 10 Hz and 300 s:
50 – 300 x ILL

## Slide 43
Monolith
liner
Thank you!